## Slide 1
SMARTBAND V001 — REV1
Firmware Development: From an Unresolved Hardware Fault
to a Working, BLE-Enabled Multi-Sensor Node
Masrur Jamil Prochchhod · 2210028
Hochschule Hamm-Lippstadt · Supervisor: Prof. Giovanni

## Slide 2
Agenda
Smartband V001 — Rev1 Firmware Development
2
01
Project Context & the Original Problem
02
Tools & Development Environment
03
Methodology — Why a Clean Rebuild
04
Building the Sensor Firmware, Stage by Stage
05
Solving the Original BLE Fault
06
Combining Sensors + BLE
07
Summary & Conclusion

## Slide 3
01
Project Context & the Original Problem
What Smartband V001 Rev1 is, and the fault this work set out to resolve
Smartband V001 — Rev1 Firmware Development
3

## Slide 4
CONTEXT
Rev1 Hardware at a Glance
Smartband V001 — Rev1 Firmware Development
4
Custom PCB built around the Texas Instruments CC2640R2F Bluetooth Low Energy SoC
LIS331DLTR
3-axis MEMS Accelerometer
I2C 0x18
MAX30205
Clinical Digital Temperature Sensor
I2C 0x48
MAX30102
Integrated Pulse-Oximetry / IR Sensor
I2C 0x57
Note: a Raspberry Pi 5 acts as a companion processor, but is entirely out of scope for this document — everything here is embedded firmware on the CC2640R2F.

## Slide 5
CONTEXT
The Problem This Work Set Out to Solve
Smartband V001 — Rev1 Firmware Development
5
!
A Long-Standing, Unresolved Fault
GAPRole_StartDevice() faults with a hardware exception, landing in
ti_sysbios_family_arm_m3_Hwi_excHandler__I
Previously investigated for roughly 20 hours, without resolution
Tentatively blamed on an RF or hardware defect in the custom PCB itself
Legacy firmware mixed BLE stack, three sensor drivers, and OLED code in one ~1,700-line file
A serious conclusion for a custom board — needed to be confirmed properly, not patched around

## Slide 6
02
Tools & Development Environment
What was used to build, flash, and debug every stage of this work
Smartband V001 — Rev1 Firmware Development
6

## Slide 7
TOOLS
Development Environment
Smartband V001 — Rev1 Firmware Development
7
Tool | Role
Code Composer Studio 12.8.1 | Editing, building, flashing, hardware debugging
TI SimpleLink CC2640R2 SDK v5.30.1.11 | Clean board files and BLE5-Stack example projects
LaunchPad + XDS110 debug probe | External JTAG programmer only — its own MCU never runs project code
CCS Hardware Debugger | Breakpoints, call-stack inspection, disassembly — the core diagnostic tool
Raspberry Pi 5 (UART, 115200 baud) | Serial terminal to observe live firmware output
nRF Connect (mobile) | Independent, external BLE advertising/connection verification

## Slide 8
03
Methodology
Why a clean rebuild was chosen over patching the existing firmware
Smartband V001 — Rev1 Firmware Development
8

## Slide 9
METHODOLOGY
A Deliberately Conservative Approach
Smartband V001 — Rev1 Firmware Development
9
1
Start Clean
Use TI's own unmodified SDK example projects — not the tangled legacy file
2
One Capability at a Time
RTOS → UART → I2C → each sensor → periodic loop, in strict order
3
Verify on Real Hardware
Rebuild and reflash after every single change, no assumptions carried forward
4
Debug, Don't Guess
Use breakpoints, call-stack, and disassembly whenever something failed
5
Delay BLE Reintroduction
Only bring BLE back once sensors were fully proven — to isolate the real cause

## Slide 10
04
Building the Sensor Firmware
Six stages, each verified on real hardware before moving to the next
Smartband V001 — Rev1 Firmware Development
10

## Slide 11
OVERVIEW
Six Stages, Tested on Hardware Every Time
Smartband V001 — Rev1 Firmware Development
11
1
RTOS Boot
Minimal TI-RTOS project, zero BLE
2
UART
Counter message to the Pi every 3s
3
I2C + Accel
LIS331DLTR WHO_AM_I read
4
Temperature
MAX30205 raw register read
5
PPG Sensor
MAX30102 Part ID read
6
Periodic
All 3 sensors, live, every 3s
Each stage rebuilt and reflashed before moving to the next — no assumptions carried forward.

## Slide 12
STAGE 1
Stage 1 — Confirming the RTOS Boots Cleanly
Smartband V001 — Rev1 Firmware Development
12
TI's built-in "empty" TI-RTOS example, imported unmodified — zero Bluetooth code
Goal: prove the chip and JTAG connection are healthy before adding anything else
RESULT
Built with 0 errors. Debugger confirmed the processor sitting inside CPUwfi() via PRCMDeepSleep() — normal, healthy RTOS idle behaviour.
WHY IT MATTERS
This was the first solid, positive proof that the CC2640R2F chip and the JTAG debug link on Rev1 were fundamentally healthy — independent of BLE entirely.

## Slide 13
STAGE 2
Stage 2 — Bug #1: Boot Hangs at PIN_init()
Smartband V001 — Rev1 Firmware Development
13
!
Symptom: execution never leaves PIN_init(BoardGpioInitTable) — confirmed via breakpoint & call-stack.
ROOT CAUSE
BoardGpioInitTable configures LEDs, buttons, and an external SPI flash chip select — hardware that exists only on the stock LaunchPad, not on Rev1's custom PCB.
FIX
const PIN_Config BoardGpioInitTable[] = {
/* Rev1: only UART + I2C kept */
UART_RX | PIN_INPUT_EN | ...,
UART_TX | PIN_GPIO_OUTPUT_EN | ...,
PIN_TERMINATE
};

## Slide 14
STAGE 2
Stage 2 — Bug #2: Hang Inside Board_initHook()
Smartband V001 — Rev1 Firmware Development
14
!
Symptom: after fixing bug #1, a new hang appears inside PIN_close(), spinning forever.
ROOT CAUSE
Board_initHook() tries to wake up, then shut down, an external SPI flash chip Rev1 does not have. The handshake never completes; PIN_close() spins forever.
FIX
void Board_initHook()
{
/* Intentionally empty --
* no ext flash on Rev1 */
}
// Result: UART counter received
// on the Pi every 3s. ✓

## Slide 15
STAGE 3
Stage 3 — I2C Bus & the LIS331DLTR Accelerometer
Smartband V001 — Rev1 Firmware Development
15
Same class of bug reappears: SDK's default I2C pins match the stock LaunchPad, not Rev1's real schematic.
 | SDK Default (LaunchPad) | Rev1 Actual Schematic
SCL | IOID_4 | IOID_5
SDA | IOID_5 | IOID_6
Fixed in both BoardGpioInitTable and I2CCC26XX_HWAttrsV1.
Result: WHO_AM_I = 0x32, consistently — matches the LIS331DLH/DLTR datasheet exactly.
✓

## Slide 16
STAGE 4-5
Stage 4 & 5 — Temperature and PPG Sensors
Smartband V001 — Rev1 Firmware Development
16
MAX30205
Temperature
temp_c = temp_raw / 256.0f
~26.8 – 26.9 °C
Stable, physically plausible room temperature across repeated samples
MAX30102
PPG / IR Sensor
Part ID register (0xFF)
0x15
Matches the documented MAX3010x family ID exactly — distinguishes it from sibling parts

## Slide 17
STAGE 6
Stage 6 — Fixing a "Torn Read" on the Accelerometer
Smartband V001 — Rev1 Firmware Development
17
Symptom: board sitting perfectly still still produced wildly swinging acceleration values.
BEFORE — 2 transactions
uint8_t xl = get_i2c_value_lis331_xl();
/* transaction #1 */
uint8_t xh = get_i2c_value_lis331_xh();
/* transaction #2 */
int16_t raw = (xh<<8)|xl;
// Sensor updates BETWEEN the two
// reads -> bytes from two DIFFERENT
// samples get combined = garbage
AFTER — 1 burst read
tx_buf[0] = OUT_X_L | 0x80;
/* auto-increment bit set */
i2c_trans.readCount = 2;
/* reads both bytes atomically */
int16_t raw =
(rx_buf[1]<<8)|rx_buf[0];
// Result: stable 10-18 mg at rest,
// changes predictably when moved

## Slide 18
STAGE 6
Stage 6 — From Static IDs to Live, Changing Data
Smartband V001 — Rev1 Firmware Development
18
get_i2c_value_max3010x_basicinit() added once at startup — sets LED current + mode
Without it: the MAX30102's LED never physically turns on; IR_RAW stays at 0
Periodic task now reads all 3 sensors together, every 3 seconds
static void SimplePeripheral_performPeriodicTask(void)
{
int16_t accel_x = get_i2c_value_lis331_accel_x();
uint16_t temp_raw = get_i2c_value_max30205_rawtemp(0x48);
uint32_t ir_raw = get_i2c_value_max3010x_ir_raw();
Display_print1(dispHandle, 13, 0, "LIS331DLTR ACCEL_X=%dmg", accel_x);
Display_print2(dispHandle, 14, 0, "MAX30205 TEMP=%d.%02dC", ...);
Display_print1(dispHandle, 15, 0, "MAX30102 IR_RAW=%lu", ir_raw);
}

## Slide 19
05
Solving the Original BLE Fault
Isolating BLE from everything else finally reveals the true root cause
Smartband V001 — Rev1 Firmware Development
19

## Slide 20
BLE INVESTIGATION
Isolating BLE From Everything Else
Smartband V001 — Rev1 Firmware Development
20
Built a second clean project: TI's official ble5stack "simple_peripheral" example, unmodified
On first boot: hit the EXACT SAME PIN_init() / Board_initHook() failures already solved in Stage 2
This proves — these are generic board-file defects, not sensor-specific bugs
Applied the identical fixes (GPIO table, Board_initHook, I2C pins) to this project
Result: firmware advanced past every prior blocking point and began advertising over BLE — independently confirmed by connecting with nRF Connect on a phone.

## Slide 21
BLE INVESTIGATION
The Real Root Cause
Smartband V001 — Rev1 Firmware Development
21
PREVIOUSLY BELIEVED
"RF or hardware defect on the custom board — the CC2640R2F radio itself is likely faulty."
ACTUALLY CONFIRMED
The radio hardware is fully functional. The fault was a board-file mismatch occurring earlier in boot than the reported crash location — the same class of bug fixed in the sensor firmware.

## Slide 22
06
Combining Sensors + BLE
Merging two verified systems surfaced new, instructive problems
Smartband V001 — Rev1 Firmware Development
22

## Slide 23
INTEGRATION
Four New Struggles During Integration
Smartband V001 — Rev1 Firmware Development
23
Header Collision
i2c_sensors.h's own Board.h collided with the BLE project's board.h on a case-insensitive filesystem — one silently skipped the other
Missing Macro
SBP_DISPLAY_TYPE, normally a compiler predefine, stopped reaching this build config after heavy Clean/rebuild cycles
Malformed Comment
A comment closed with "*" instead of "*/" silently absorbed several real lines of working code
Competing UART Handles
A second raw UART_open() competed with the Display driver, which already owned the physical UART peripheral

## Slide 24
INTEGRATION
Fix — Reuse the Proven Display Path, Not a New UART Handle
Smartband V001 — Rev1 Firmware Development
24
BLE stack's own status messages ("Initialized", "Adv Set 1 Enabled") already reached the Pi correctly via Display_print*()
A second, independently-opened raw UART handle for sensor data did NOT — it silently competed for the same physical peripheral
Fix: route sensor output through the exact same, already-working dispHandle instead
dispHandle = Display_open(SBP_DISPLAY_TYPE, NULL);
if (dispHandle != NULL) {
I2C_init();
uint8_t lis_whoami = get_i2c_value_lis331_whoami();
Display_print1(dispHandle, 12, 0,
"TEST: LIS331_WHOAMI=0x%02x", lis_whoami);
}
// Result received on the Pi: TEST: LIS331_WHOAMI=0x32 ✓

## Slide 25
INTEGRATION
Final Result
Smartband V001 — Rev1 Firmware Development
25
One firmware. Three verified sensors. Live BLE connection.
Periodic loop reads LIS331DLTR, MAX30205, and MAX30102 every 3 seconds
Output printed as clear, labelled text: "ACCEL_X=…mg", "TEMP=…C", "IR_RAW=…"
Runs independently of BLE connection state — starts unconditionally at boot
Device simultaneously advertises and accepts BLE connections (verified via nRF Connect)

## Slide 26
07
Summary & Conclusion
Every root cause, every fix, and what this means going forward
Smartband V001 — Rev1 Firmware Development
26

## Slide 27
SUMMARY
Complete Summary of Root Causes & Fixes
Smartband V001 — Rev1 Firmware Development
27
Symptom | Root Cause | Fix
PIN_init() hangs at boot | GPIO table configured non-existent LaunchPad hardware | Stripped to Rev1's real UART + I2C pins
PIN_close() hangs in Board_initHook() | Tried managing an ext. SPI flash chip Rev1 lacks | Board_initHook() emptied
I2C reads fail/garbage | Default I2C pins matched LaunchPad, not Rev1 | Corrected pins in GPIO table + I2C HWAttrs
Accel jitters at rest | Torn read across two I2C transactions | Single burst read w/ auto-increment
"BLE hardware fault" (original issue) | Same board-file mismatches, earlier in boot | Same fixes applied — BLE now works
Sensor data silent in merged project | Header collision, missing macro, bad comment, dual UART | Each isolated & fixed individually

## Slide 28
SUMMARY
Conclusion
Smartband V001 — Rev1 Firmware Development
28
A 20-hour, unresolved fault became a fully documented, fixed root cause
The recurring theme: SDK board files assume LaunchPad hardware, not Rev1's real PCB
This pattern-recognition is directly reusable for Rev2 and future hardware revisions
Systematic, hardware-verified, one-variable-at-a-time debugging outperformed patching a large tangled codebase

## Slide 29
Systematic isolation testing turned an unresolved,
20-hour mystery into a documented, fixed root cause.
Thank you