## Slide 1
Health Wearable Device
Firmware Architecture
& Code Analysis Report
Band01_Rev1 · Project Work — Task 2
Prepared by:
Masrur Jamil Prochchhod
Institution:
Hochschule Hamm-Lippstadt (HSHL)
Matriculation:
2210028
Date:
27 May 2026
70
Source Files
8
Directories
1,647
Lines (main)
13
Report Sections
4
RTOS Tasks
1 / 17

## Slide 2
What Is This Firmware?
2 / 17
The firmware is the software that runs directly on the CC2640R2F microcontroller — it is the "brain" of the smartband.
It is NOT a phone app
It runs on bare metal inside the wristband chip itself, not on Android/iOS. There is no operating system like Windows — only a lightweight RTOS (SYS/BIOS).
It talks to hardware directly
Via I²C, it reads MAX30102 (heart rate), MAX30205 (temperature) and LIS331 (motion). It controls every GPIO pin on the PCB.
It transmits data wirelessly
Every 350 ms, sensor data is packaged into a 6-byte BLE GATT notification and sent to a smartphone or hospital gateway via BLE 5.1.
It manages power
It controls the LP5907 regulator EN pins to power down sensors, and uses deep sleep between BLE events to achieve 73-hour battery life.
Built on: TI SimpleLink CC2640R2 SDK · SYS/BIOS RTOS · TI BLE Stack · Code Composer Studio v10+
Teaching note — Unlike desktop software, embedded firmware has no loader — it boots directly from flash memory. Every line of code must fit within 128 KB total flash on this chip.

## Slide 3
Development Environment & Repository Structure
3 / 17
Required Tools & SDKs
CCS v10+
Eclipse-based TI IDE — compile, link, flash, debug
SimpleLink SDK
BLE stack + hardware drivers for CC2640R2F
TI ARM Compiler
Included with CCS — targets ARM Cortex-M3
BLE Stack (ROM)
Pre-compiled — stored in FlashROM_StackLibrary/
SYS/BIOS RTOS
Real-time OS — part of TI SDK
XDS110 Probe
USB JTAG debugger → connects to P1 header on PCB
Repository Folder Map
Startup/
Boot, CCFG, RTOS entry point
Application/
Sensors, OLED, BLE app logic
PROFILES/
BLE GATT service definitions
Include/
Shared header files
FlashROM_Stack/
Pre-compiled BLE stack (do not edit)
TOOLS/
SYS/BIOS config (app_ble.cfg)
targetConfigs/
CCS debug target for CC2640R2F
BOM/
Aisler Bill of Materials PDF
Teaching note — CCS is mandatory for compilation. Source files can be read in VS Code, but building, flashing and SDK path configuration must be done inside CCS.

## Slide 4
Boot Sequence — Startup/main.c
4 / 17
8 Steps before BIOS_start()
1
RegisterAssertCback()
Register BLE error handler
2
PIN_init()
Initialise all GPIO pins
3
VIMSModeSet()
Enable instruction cache
4
ICall_init()
Set up inter-task messaging
5
ICall_createRemoteTasks()
Start BLE stack (Priority 5)
6
GAPRole_createTask()
Create GAP role (Priority 5)
7
SimplePeripheral_createTask()
Create app task (Priority 2)
8
BIOS_start()
Hand control to RTOS — never returns
int main() {
RegisterAssertCback(AssertHandler);
PIN_init(BoardGpioInitTable);
ICall_init();
ICall_createRemoteTasks(); // BLE Pri 5
GAPRole_createTask(); // GAP Pri 5
SimplePeripheral_createTask(); // App Pri 2
//App_createTask(); // DISABLED
//OledThread_createTask(); // DISABLED
BIOS_start(); // never returns
}
AppThread & OledThread exist in the repo but are commented out in main.c — the code is ready, just not yet activated.
ccfg_app_ble.c — chip-level flash config (bootloader, power, radio trim). Compiled separately, never modified by user.
Teaching note — BIOS_start() is the point of no return — the RTOS scheduler takes over. Priority 5 BLE tasks will always pre-empt the Priority 2 app task when radio events occur.

## Slide 5
How the Main App Task Works — SimplePeripheral
5 / 17
Chip powers on
main() runs
Init once
SimplePeripheral_init()
Start 350ms clock
SYS/BIOS Clock object
RTOS scheduler
task waits for events
↺ repeats every 350 ms
Phone notified
GATT notification sent
Update BLE char
CHAR1 ← 6 bytes
Read sensors
I²C (placeholder now)
Clock fires
every 350 ms
Key timing constants:
ADV_INTERVAL
100 ms — BLE advertising
PERIODIC_EVT
350 ms — Sensor poll
MIN_CONN
100 ms — Min BLE conn
MAX_CONN
1000 ms — Max BLE conn
TIMEOUT
10 s — Supervision
Teaching note — The 350 ms period was chosen to match the research paper's power budget of 2.032 mA average. Shorter interval = more radio activity = shorter battery life.

## Slide 6
simple_peripheral.c — Core Sensor & BLE Loop
6 / 17
SmartBand_periodicFxn() — runs every 350 ms
// Fires every 350 ms via SYS/BIOS Clock
void SmartBand_periodicFxn(void) {
GAPRole_GetParameter(GAPROLE_STATE, &state);
if (state == GAPROLE_CONNECTED) {
i2c_signal_data = 0x7788; // ← placeholder
// ACTIVATE: get_i2c_value_max30205_rawtemp()
uint8_t arr[] = {0,1,2,0,upper,lower};
SimpleProfile_SetParameter(
SIMPLEPROFILE_CHAR1, 6, arr);
}
}
Button handling — buttonCallbackFxn()
// GPIO interrupt — fires on button press
void buttonCallbackFxn(PIN_Handle h, PIN_Id id) {
PIN_setConfig(h, PIN_BM_IRQ, id|PIN_IRQ_DIS);
if (id==Board_BUTTON0) button0State ^= 1;
if (id==Board_BUTTON1) button1State ^= 1;
// Re-enabled at end of periodicFxn()
}
What each part does
GAPRole_GetParameter()
Checks if a phone is currently connected. Sensor data is only sent when BLE is connected — saving power when no phone is nearby.
0x7788 placeholder
The current firmware transmits this hardcoded value instead of real sensor data. It proves BLE works before sensors are enabled.
SimpleProfile_SetParameter()
Writes the 6-byte array into GATT CHAR1 (UUID 0xFFF1). The TI BLE stack then automatically sends a GATT notification to the phone.
buttonCallbackFxn()
Runs in interrupt context (not RTOS task context). Interrupt is disabled on entry to debounce — re-enabled 350 ms later by the clock.
Teaching note — SimplePeripheral_init() is called once at boot to register GATT, configure BLE params, set up button interrupts, and draw the OLED splash screen.

## Slide 7
I²C Sensor Driver — i2c_sensors.c (437 lines)
7 / 17
Standard I²C Read Pattern
I2C_Params params;
I2C_Transaction txn;
uint8_t txBuf[1] = {REG_ADDR};
uint8_t rxBuf[1];
params.bitRate = I2C_400kHz;
txn.slaveAddress = 0x57; // MAX30102
txn.writeBuf=txBuf; txn.writeCount=1;
txn.readBuf =rxBuf; txn.readCount=1;
handle = I2C_open(Board_I2C0, &params);
if (I2C_transfer(handle, &txn))
return rxBuf[0];
I2C_close(handle);
Temperature conversion (MAX30205):
uint16_t raw = (rxBuf[0]<<8 | rxBuf[1]);
float degC = raw * 0.00390625f; // 1/256°C
Sensor Functions Available
MAX30102
0x57
get_i2c_value_max3010x_id()
Read PART_ID — chip health check
MAX30102
0x57
get_i2c_value_max3010x_basicinit()
Set LED current to 6.2 mA
LIS331
0x18
get_i2c_value_lis331_powerup()
Enable all axes, normal power
LIS331
0x18
get_i2c_value_lis331_whoami()
Returns 0x33 (verify vs datasheet!)
LIS331
0x18
get_i2c_value_lis331_xh() / xl()
X-axis acceleration high/low byte
MAX30205
0x48
get_i2c_value_max30205_rawtemp()
Raw 16-bit temperature register
⚠ WHO_AM_I discrepancy: firmware uses 0x33 but LIS331DL datasheet specifies 0x3B. Verify the exact LIS331 variant on PCB before flashing — a mismatch causes silent sensor init failure.
Teaching note — All I²C functions open and close the bus per-transaction. In production, keep the handle open during sensor polling to reduce latency and overhead.

## Slide 8
How I²C Communication Works — Explained
8 / 17
I²C (Inter-Integrated Circuit) — 2 wires, many devices, one master
SCL (clock)
SDA (data)
CC2640R2F
(Master)
DIO_5=SCL
DIO_6=SDA
MAX30102
HR/SpO₂
addr: 0x57
MAX30205
Temperature
addr: 0x90
LIS331
Accelerometer
addr: 0x19
R103/R104 — 10 kΩ pull-up resistors keep SCL and SDA HIGH when idle (I²C is open-drain — devices can only pull LOW)
A typical I²C read transaction — step by step:
①
Master sends START + slave address + R/W bit
②
Slave responds with ACK (acknowledgement)
③
Master sends register address to read
④
Slave sends 1–2 bytes of data back
⑤
Master sends STOP — bus released
Why I²C for this wearable?
Only 2 wires (SCL + SDA) connect all 3 sensors + OLED display — critical on a 34×40 mm PCB where every trace matters. The CC2640R2F is bus master, polling each sensor in turn using unique 7-bit addresses.
Teaching note — The 400 kHz fast-mode I²C used here can read 2 bytes from MAX30205 in ~40 µs — fast enough for the 350 ms polling period while leaving the CPU free for BLE tasks.

## Slide 9
OLED Display — oled.c + oled_thread.c
9 / 17
SSD1306 Driver — Public API (oled.c, 334 lines)
oledInit()
22-byte SSD1306 init sequence
oledFill(data)
Fill all 8 pages × 128 columns
oledWriteString(x,y,str)
Render ASCII text via ucFont[]
oledDrawPic(pic,w,h,x,y)
Binary bitmap from flash memory
oledSetPosition(x,y)
Move write cursor (page + column)
oledShutdown()
Send 0xAE — panel off (saves power)
oled_thread.c — Dedicated Task (183 lines)
Status: DISABLED in main.c — code complete, not activated
Priority:
1 — display is non-critical, always yields to BLE
Stack:
800 bytes
Pattern:
Event-driven queue — waits on OLED_EVENT_SCREEN_UPDATE
Messages:
MEDIC_PIC, HEART_PIC, BUTTON_PRESS, DATA_HEX
// Boot splash screen (currently active)
oledInit();
oledFill(0x00); // clear screen
oledWriteString(0,0,"Smart Band V001");
Once enabled: oled_thread displays live HR, SpO₂, temp and motion data in real time
Teaching note — Separating display into its own task (oled_thread) prevents OLED I²C transactions from blocking the BLE task — a core embedded multitasking principle.

## Slide 10
BLE GATT Profile — Service 0xFFF0
10 / 17
Five Characteristics — What the Smartphone Sees
Char
UUID
Length
Access
Current Use
CHAR1
0xFFF1
6 bytes
R/W
Sensor array: [MAX3010x_id, LIS_whoami, LIS_xh, LIS_xl, temp_upper, temp_lower]
CHAR2
0xFFF2
1 byte
Read
Status byte: bit[0]=button0, bit[4]=button1, BLE state
CHAR3
0xFFF3
1 byte
R/W
General purpose — reserved for future sensor data
CHAR4
0xFFF4
1 byte
Notify
Push-notification channel — phone receives alerts without polling
CHAR5
0xFFF5
5 bytes
R/W
Extended buffer — reserved for future multi-byte values
End-to-End Data Flow — Sensor to Phone
i2c_sensors.c
read sensor
pack into
6-byte array
SetParameter
(CHAR1)
BLE stack
auto-notify
Smartphone
reads CHAR1
Every 350 ms
Teaching note — GATT = Generic Attribute Profile. Any BLE scanner app (nRF Connect on Android/iOS) can connect and read CHAR1 live — no custom app needed during development.

## Slide 11
Understanding BLE & GATT — How Wireless Data Works
11 / 17
BLE = Bluetooth Low Energy — designed for small data bursts from battery-powered devices, not continuous audio streaming like classic Bluetooth.
The CC2640R2F advertises every 100 ms ("I'm here!"). A phone connects, then receives GATT notifications every 350 ms containing the sensor data.
GATT Data Model — how data is organised:
Device (Band01_Rev1)
Service 0xFFF0 (like a folder)
CHAR1 0xFFF1 — 6 bytes — sensor data array
CHAR2 0xFFF2 — 1 byte — button state
CHAR4 0xFFF4 — 1 byte — Notify (phone gets alerts without polling)
Security: current build = Just-Works pairing (no auth) — any BLE device can connect. For clinical use, Passkey or LE Secure Connections required.
Teaching note — BLE GATT is like a USB stick with folders (Services) and files (Characteristics). The phone reads the 'file' (CHAR1) every 350 ms — no custom protocol or app code needed.

## Slide 12
BLE Stack Layers & Memory Map
12 / 17
BLE Protocol Stack — FlashROM_StackLibrary/
Pre-compiled by TI · Do NOT modify
GAP
Generic Access Profile
Advertising, scanning, connections
GATT
Generic Attribute Profile
Service & characteristic layer
ATT
Attribute Protocol
GATT data R/W/Notify at byte level
SMP
Security Manager
Pairing, bonding, key exchange
L2CAP
Logical Link Control
Channel mux, segmentation
HCI
Host Controller Interface
App ↔ BLE radio bridge
RF
2.4 GHz Radio Driver
CC2640R2F RF core control
CC2640R2F Memory Map (128 KB Flash / 20 KB SRAM)
~70 KB flash
App Image
main, SimplePeripheral, sensors, OLED, GATT
~50 KB flash
BLE Stack
HCI, L2CAP, ATT, SMP, GAP, RF driver
88 bytes
CCFG Region
ccfg_app_ble.c — bootloader & radio trim
~12 KB RAM
App SRAM
Heap, task stacks, GATT database
~8 KB RAM
Stack SRAM
BLE queues, HCI buffers, connections
Teaching note — App and BLE stack are two separately linked binaries sharing one 128 KB flash. Exact sizes are in Debug/smart_band_v001_app.map after a CCS build.

## Slide 13
RTOS Architecture — SYS/BIOS Task Model
13 / 17
Task Table — Pre-emptive Fixed-Priority Scheduling
Task
Priority
Stack
Status
File
Responsibility
Notes
BLE Stack
5 ★
Internal
Active
FlashROM/
Radio, advertising, connections
Highest priority — always pre-empts app
GAPRole
5
Internal
Active
peripheral.c
GAP connection events
Handles BLE peripheral role
SimplePeripheral
2
800 B
Active
simple_perip…
Sensor reads + BLE updates
Core loop — every 350 ms
OledThread
1
800 B
Disabled
oled_thread.c
Event-driven display
Commented out — ready to enable
AppThread
1
700 B
Disabled
app_thread.c
Secondary sensor/signal
Scaffold — awaiting sensor integration
SYS/BIOS Primitives Used in This Firmware:
Clock
Periodic timers
(350 ms poll)
Event
Task sync
(OLED events)
Queue
Inter-task messages
(OLED queue)
Semaphore
Mutual exclusion
(resource locks)
Task
Thread definition
(each RTOS task)
Teaching note — SYS/BIOS uses fixed-priority pre-emptive scheduling — NOT POSIX. Priority 5 BLE tasks will always pre-empt the Priority 2 app task mid-execution when radio events occur.

## Slide 14
Power Architecture in Firmware
14 / 17
Active / Connected
BLE:
BLE connected + 350 ms notifications
Sensors:
All sensors powered
~2.0 mA
Advertising
BLE:
Periodic BLE adv (100 ms interval)
Sensors:
Can be gated off
< 1 mA
Deep Sleep
BLE:
32 kHz Y2 crystal maintains schedule
Sensors:
All powered down
< 1 µA
Battery Life Calculation
150 mAh ÷ 2.032 mA = 73.8 hours ≈ 73+ hours
Source: Pinheiro et al. (2021) — measured 2.032 mA avg at 350 ms BLE interval
POWER_SAVING compile flag:
Controls deep sleep permission. When enabled, MCU enters standby between BLE events. The 32 kHz crystal Y2 keeps waking it at precise intervals.
Teaching note — LP5907 EN pins are wired to CC2640R2F GPIOs — firmware can cut sensor power entirely during BLE advertising, achieving the <1 µA standby current target.

## Slide 15
Debugging — JTAG, Assertions & Recommended Improvements
15 / 17
Two Debug Paths
① JTAG via XDS110 probe + P1 header
Connect XDS110 USB probe to P1 header (18-pin)
· TCK → DIO_3 · TMS → DIO_4 · TDI + TDO
In CCS: set breakpoints, step through code line-by-line, inspect registers, watch variables live, measure current
② BLE Stack Assertion Handler
RegisterAssertCback(AssertHandler) — registered in main()
Fires when BLE stack detects internal violations (wrong HCI state, message buffer exhaustion)
Current behaviour: loops forever — visible to debugger but silent to user without JTAG
Recommended Improvement — Visible Assert
Current AssertHandler loops silently. Improved version displays the error code on the OLED so faults are visible without a JTAG probe attached:
void AssertHandler(uint8 cause,
uint8 subcause) {
char buf[24];
oledFill(0x00);
oledWriteString(0,0,"ASSERT ERROR");
snprintf(buf,sizeof(buf),
"cause=%02x sub=%02x",
cause, subcause);
oledWriteString(0,2,buf);
while(1); // attach JTAG here
}
This is a recommended Task 3 improvement — diagnose faults in the field without a laptop.
Teaching note — JTAG debug is the primary tool during development. The assertion handler becomes essential once the device is deployed away from a desktop — it's your last line of defence.

## Slide 16
Firmware–Hardware Pin Correspondence
16 / 17
Every DIO pin in firmware maps to a physical component on Band01_Rev1 (Task 1 reference)
HW Component
DIO
Code Ref
Code File
Purpose
Status
I²C SCL (all sensors+OLED)
DIO_5
Board_I2C0 SCL
i2c_sensors.c, oled.c
I²C clock 400kHz — shared by all 4 devices
Active
I²C SDA (all sensors+OLED)
DIO_6
Board_I2C0 SDA
i2c_sensors.c, oled.c
I²C data bidirectional
Active
MAX30102 interrupt
DIO_8
(not handled yet)
simple_peripheral.c
HR data-ready — not wired in firmware
Pending
LIS331 interrupt 1
DIO_9
(not handled yet)
simple_peripheral.c
Motion event interrupt 1
Pending
LIS331 interrupt 2
DIO_2
(not handled yet)
simple_peripheral.c
Motion event interrupt 2
Pending
SW101 Button
DIO_0
Board_BUTTON0
simple_peripheral.c
Falling-edge ISR, toggles state → CHAR2
Active
SW102 Button
DIO_1
Board_BUTTON1
simple_peripheral.c
Falling-edge ISR, toggles state → CHAR2
Active
JTAG TCK (P1 header)
DIO_3
JTAG TCK
targetConfigs/*.ccxml
CCS debug probe clock
Active
JTAG TMS (P1 header)
DIO_4
JTAG TMS
targetConfigs/*.ccxml
CCS debug mode select
Active
24 MHz Crystal Y1
X24M_P/N
BLE radio clock
FlashROM_Stack/
Required for BLE RF synthesis
Active
Teaching note — Interrupt pins DIO_8/9/2 are physically wired on the PCB but not yet handled in firmware. Activating them replaces polling with interrupt-driven reads — critical for power efficiency.

## Slide 17
Current Status & Key Takeaways
Band01_Rev1 Firmware — Task 2 | Masrur Jamil Prochchhod | HSHL 2026
Implementation Status
BLE advertising + connection
Complete
GATT Service 0xFFF0 (5 chars)
Complete
OLED hardware driver
Complete
Splash screen at boot
Complete
Button GPIO interrupts
Complete
I²C driver for all sensors
Complete
350 ms periodic BLE update
Complete
Live MAX30205 temperature
Pending
Live MAX30102 HR / SpO₂
Pending
Live LIS331 accelerometer
Pending
OLED live display
Pending
ESPRIT HR algorithm
Not started
BLE security hardening
Not started
CC2640R2F + SYS/BIOS
ARM Cortex-M3 + BLE 5.1 SoC running TI SYS/BIOS RTOS — 5 tasks, fixed-priority pre-emptive scheduling
Infrastructure Complete
BLE GATT, I²C drivers, OLED, button handling all done — 3 lines of code activate live sensors
Placeholder Active
Device currently transmits {0,1,2,0,0x77,0x88} — real sensor calls are commented out and ready
Dual-Binary Flash
App (~70 KB) + BLE stack (~50 KB) share 128 KB flash — memory map in .map file after CCS build
73-hour Battery Life
2.032 mA avg × 150 mAh = 73.8 h · POWER_SAVING flag + LP5907 EN pins enable <1 µA deep sleep
ESPRIT Algorithm Next
Research paper targets ESPRIT via Hilbert Transform for HR estimation at 100 Hz — not yet in firmware
Next: Task 3 — Build in CCS, flash to hardware, activate live sensor reading, verify with nRF Connect
17 / 17