## Slide 1
HARDWARE EQUIPMENT
RECOMMENDATION REPORT
Band01_Rev1 Smartband · Task 3 Preparation
Submitted to: Prof. Dr. Javidi da Costa, Joao Paulo Prepared by: Masrur Jamil Prochchhod Matriculation: 2210028 Date: 28 May 2026
Current Status: PCB manufactured & available · Firmware compiled (0 errors, 28 May 2026) · No debug probe · No power supply defined
HSHL Internship Project · June 2026

## Slide 2
CRITICAL: Power Architecture — Read Before Connecting Anything
⚠ An incorrect power connection will permanently damage the LP5907 LDO regulator on the PCB. AMS1117-3.3 modules MUST NOT be used — they will destroy U101.
P1 Header Power Pins — confirmed from Altium schematic:
Pin 12
VBAT
Direct input to LP5907 U101 and U102
✓ CORRECT — connect power here
Pin 17
GND
Ground — connect negative of any power source here
✓ CORRECT — connect GND here
Pin 18
3V3
OUTPUT of LP5907 U101 — do NOT inject power here
✗ WRONG — damages U101 if powered
Pin 16
N/C
Not connected in schematic
✗ Do not use
Why AMS1117-3.3 damages the board: It outputs 3.3V directly into Pin 18 (3V3 net) — the OUTPUT of U101. LP5907 does not permit reverse current on its output. This destroys U101.
Hardware Equipment Recommendation Report · Band01_Rev1 · Task 3 Preparation · HSHL 2026

## Slide 3
DEBUG PROBE RECOMMENDATIONS — 3 Options Ranked
1
RECOMMENDED
SEGGER J-Link EDU Mini
Part: 8.08.91
JTAG + SWD — CC2640R2F uses JTAG
EDU license — valid for HSHL academic use
Compact card form factor + 10-pin ribbon
Natively supported by CCS
Standalone flash commander tool included
€68.96 · mouser.de (829-8.08.91)
2
ALTERNATIVE
LAUNCHXL-CC2640R2
TI LaunchPad kit
Uses onboard XDS110 as debug probe
Remove isolation jumpers before use
No CCS config changes needed (XDS110 default)
Bulkier — full dev board for probe use only
Useful if CC2640R2F reference needed later
€32.42 · mouser.de (LAUNCHXL-CC2640R2)
3
ALTERNATIVE
SEGGER J-Link BASE
Part: 8.08.28
Identical function to Option 1 for this project
Commercial license — not needed for HSHL
Larger form factor, 20-pin JTAG connector
No technical advantage over EDU Mini here
Only if lab policy requires commercial license
€589.05 · mouser.de (829-8.08.28)
Hardware Equipment Recommendation Report · Band01_Rev1 · Task 3 Preparation · HSHL 2026

## Slide 4
JTAG WIRING — P1 Header Connection (Identical for All 3 Probe Options)
Connect probe to P1 header using Dupont M-F jumper wires:
Probe Signal
P1 Pin
Purpose
VTref
Pin 18 (3V3)
Voltage reference sense only — does NOT supply power to board
GND
Pin 17 (GND)
Ground connection
TDI
Pin 11
JTAG Test Data In
TMS
Pin 9
JTAG Test Mode Select
TCK
Pin 7
JTAG Test Clock
TDO
Pin 13
JTAG Test Data Out
nRESET
Pin 15
Target reset line
J-Link CCS config: targetConfigs/CC2640R2F.ccxml → change Connection from 'XDS110' to 'SEGGER J-Link Emulator' → Save. LaunchPad: No CCS changes needed.
Hardware Equipment Recommendation Report · Band01_Rev1 · Task 3 Preparation · HSHL 2026

## Slide 5
POWER SUPPLY RECOMMENDATIONS — Connect to P1 Pin 12 (VBAT)
1 RECOMMENDED
Single-Cell LiPo Battery
3.7V · 150mAh · Bare wire leads
Spec:
Single-cell LiPo, 3.7V nominal, 150mAh
Connect:
Red wire (+) → P1 pin 12 (VBAT)
Black wire (−) → P1 pin 17 (GND)
Why best:
Exactly how board was designed. Delivers 73+ hours at 2.032mA avg. Required for final wearable demo.
Lacks:
Needs TP4056 charger module between sessions (~€1)
Price:
€4.99 · reichelt.de
2 ALTERNATIVE
Adjustable Bench Supply
Set to 3.7V · 200mA+ rated · P1 pin 12
Spec:
Adjustable, 3.3–3.8V, ≥200mA current
Connect:
Red lead → P1 pin 12 (VBAT) | Set to 3.7V
Black lead → P1 pin 17 (GND) | Current limit: 150mA
Why it works:
Simulates LiPo at VBAT. Stable voltage, no drop. Easy power cycling during dev sessions.
Lacks:
Board must stay on desk — not suitable for wearable demo. May need buck converter if min output >5V.
When:
Initial flashing & first sensor activation — stable voltage more important than portability
⚠ NEVER connect both LiPo and bench supply to VBAT simultaneously — two sources on the same net will conflict and damage the battery and/or LP5907 regulators.
Hardware Equipment Recommendation Report · Band01_Rev1 · Task 3 Preparation · HSHL 2026

## Slide 6
REQUIRED ACCESSORIES & COMPLETE ORDER LIST
Required regardless of which probe or power option is chosen:
Dupont Jumper Wires M-F 20cm (pack of 40)
Connect probe to P1 header (7 wires for JTAG) + power supply to VBAT/GND
amazon.de
€8.49
USB-A Cable
Connect J-Link EDU Mini or LaunchPad to laptop USB port
Any supplier
€1.20
TP4056 LiPo Charger Module (optional)
Recharge LiPo between test sessions — Input: USB 5V, charges single-cell safely
amazon.de
€6.68
Complete Items to Order:
1 — Essential
SEGGER J-Link EDU Mini (8.08.91)
antratek.de / mouser.de
€68.96
2 — Essential
LiPo 3.7V 150mAh bare leads
reichelt.de
€4.99
3 — Essential
Dupont M-F jumper wires (×40)
amazon.de
€8.49
4 — Essential
USB-A cable
Any supplier
€1.20
5 — Recommended
TP4056 LiPo charger module
amazon.de
€6.68
Hardware Equipment Recommendation Report · Band01_Rev1 · Task 3 Preparation · HSHL 2026

## Slide 7
COMPLETE BUILD & FLASH PROCEDURE
✓ Already Completed (28 May 2026)
1
Clone repo — TOOLS/build_config.opt and Include/gapbondmgr.h now fixed
2
Import & build BLE4 stack library (workspace_v13) from blestack SDK examples
3
Copy 3 files (.lib, lib_linker.cmd, ble_r2.symbols) to C:\FlashROM_Library\
4
Build smart_band_v001_app in workspace_v12 — 0 errors ✓
→ Still Required (after items arrive)
5
Install SEGGER J-Link Software from segger.com (USB drivers + flash commander)
6
In CCS: targetConfigs/CC2640R2F.ccxml → Connection → 'SEGGER J-Link Emulator'
7
Set supply to 3.7V / connect LiPo → P1 pin 12 (VBAT) + pin 17 (GND)
8
Connect probe to P1 header using JTAG wiring table
9
In CCS: Run → Debug → firmware flashes → press Play to run
10
Verify on smartphone nRF Connect: 'Simple BLE Peripheral' → CHAR1 (0xFFF1) transmitting
Hardware Equipment Recommendation Report · Band01_Rev1 · Task 3 Preparation · HSHL 2026

## Slide 8
SUMMARY — Items to Order
Debug Probe
SEGGER J-Link EDU Mini (Part 8.08.91)
€68.96
Essential
Power
LiPo 3.7V 150mAh bare leads
€4.99
Essential
Wiring
Dupont M-F jumper wires 20cm (×40)
€8.49
Essential
Cable
USB-A cable
€1.20
Essential
Accessory
TP4056 LiPo charger module
€6.68
Recommended
Raspberry Pi: No additional hardware purchase needed — connects wirelessly via BLE Python (bluepy/bleak) to CHAR1 UUID 0xFFF1 every 350ms.
Band01_Rev1 Smartband · Masrur Jamil Prochchhod · Matriculation: 2210028 · HSHL 2026