## Slide 1
FHIR Integration Prospects
Smartband V001
Utilizing HL7 FHIR R4 Standards for Health Data Interoperability
Masrur Jamil Prochchhod · Hochschule Hamm-Lippstadt (HSHL) · June 2026 · Submitted to: Prof. Dr. Javidi da Costa, Joao Paulo

## Slide 2
What We Will Cover Today
Smartband V001 — FHIR Integration | HSHL | Masrur Jamil Prochchhod
This presentation covers the full roadmap for integrating HL7 FHIR R4 health data standards into the Smartband V001 project — from sensor hardware to hospital EHR integration.
01
What is HL7 FHIR and why it matters for wearables
02
How every Smartband sensor maps to an international LOINC code
03
The four-layer FHIR system architecture
04
Clinical workflow — how doctors interact with FHIR data
05
Future sensors planned for Band01_Rev1
06
Five-phase implementation roadmap to full compliance
07
Data privacy, GDPR, and SMART on FHIR authentication
08
Recommended next steps and procurement list

## Slide 3
What is HL7 FHIR? — The Universal Language for Health Data
Smartband V001 — FHIR Integration | HSHL | Masrur Jamil Prochchhod
HL7 FHIR R4 (Fast Healthcare Interoperability Resources) is the international standard published by Health Level Seven International for exchanging electronic health records between any system, anywhere in the world.
The Problem FHIR Solves
Before FHIR, every hospital system, health app, and medical device used its own proprietary data format. A reading from one wearable could not be understood by a hospital's software without expensive custom integration work. FHIR replaces this chaos with a single, agreed-upon format that every modern health system speaks natively.
How it Works
FHIR breaks health data into modular objects called Resources. Each resource represents one clinical concept — a patient, a measurement, a diagnosis. Resources are transmitted as JSON over standard HTTP (REST API), making them readable by any programming language or platform.
Key FHIR Resources Used in Smartband V001
Patient
Stores the wearer's demographics, age, weight, height, and device assignment
Observation
Every single sensor reading — HR, temperature, SpO2, acceleration — as a structured data object
Bundle
A container that groups multiple Observations together into one API response
Condition
Records a detected health condition or alert — e.g. elevated heart rate episode
CarePlan
The doctor's monitoring plan — thresholds, instructions, follow-up schedule

## Slide 4
Why FHIR for Smartband V001? — Six Key Reasons
Smartband V001 — FHIR Integration | HSHL | Masrur Jamil Prochchhod
Without FHIR, the Smartband's data is a proprietary island. With FHIR, it becomes part of the global health data ecosystem — readable by any hospital, app, or research platform in the world.
Interoperability
Works with any EHR or health app worldwide
FHIR-compliant data can be consumed by Epic, Cerner, OpenMRS, and thousands of other systems without writing a single line of custom integration code. One standard, infinite connections.
Clinical Validity
LOINC + UCUM ensure correct interpretation
Every sensor reading carries an internationally agreed code (LOINC) and unit (UCUM). A heart rate reading from Smartband V001 means exactly the same thing to a doctor in Germany as it does in Japan or the USA.
Research Ready
Direct import into research platforms
FHIR-formatted data can be loaded directly into clinical research databases like the N3C COVID Cohort or hospital analytics platforms, enabling Smartband data to contribute to real medical studies.
Regulatory Alignment
EU MDR and FDA increasingly require FHIR
The EU Medical Device Regulation (MDR 2017/745) and the US FDA both increasingly require or strongly recommend FHIR compliance for connected medical devices. Building it now prevents costly retrofits later.
EHR Integration
Connects to Epic, Cerner, OpenMRS directly
Because FHIR is the API standard for modern EHRs, Smartband V001 data can flow directly into a patient's hospital record — giving clinicians a complete longitudinal health picture that includes wearable data.
Clinical Workflow
Enables structured doctor-patient workflows
FHIR enables doctor dashboards, patient portals, structured care plans, and subscription-based real-time alerts — turning raw sensor data into a clinical-grade remote monitoring system.

## Slide 5
Sensor → FHIR Mapping — LOINC Codes & UCUM Units
Smartband V001 — FHIR Integration | HSHL | Masrur Jamil Prochchhod
LOINC (Logical Observation Identifiers Names and Codes) is a universal database of codes for medical measurements. UCUM standardizes the units. Together they ensure that a heart rate of 75 bpm from Smartband V001 is understood identically by every hospital system globally.
What is a LOINC Code?
A LOINC code is a unique number assigned to a specific clinical measurement. For example, 8867-4 always means Heart Rate, measured in beats per minute, anywhere in the world. It is maintained by the Regenstrief Institute and used in over 168 countries.
What is UCUM?
UCUM (Unified Code for Units of Measure) standardizes how units are written. It ensures '/min' always means beats per minute, 'Cel' always means degrees Celsius, and '[g]' always means G-force — removing any ambiguity when data crosses system boundaries.
Example FHIR Observation for Heart Rate:
{ "resourceType": "Observation",
"code": { "coding": [{ "system": "http://loinc.org",
"code": "8867-4", "display": "Heart rate" }] },
"valueQuantity": { "value": 75, "unit": "/min" } }
Measurement | Sensor | LOINC | Unit | Status
Heart Rate | MAX30102 | 8867-4 | /min | On PCB ✓
SpO2 | MAX30102 | 2708-6 | % | On PCB ✓
Body Temperature | MLX90632 | 8310-5 | Cel | On PCB ✓
Acceleration | MPU-6050 | 80493-0 | [g] | On PCB ✓
Step Count | MPU-6050 | 55423-8 | steps | Calculated
Calories | Calculated | 41981-2 | kcal | Calculated
Stress Level | GSR/EDA | 74767-6 | score | Future HW
Blood Pressure | PPG/Cuff | 55284-4 | mm[Hg] | Future HW
ECG | AD8232 | 11524-6 | mV | Future HW

## Slide 6
Four-Layer FHIR Architecture — From Sensor to Clinician
Smartband V001 — FHIR Integration | HSHL | Masrur Jamil Prochchhod
The Smartband V001 FHIR architecture has four distinct layers. The critical transformation happens at Layer 3 — this is where raw sensor numbers become internationally standardized FHIR resources that any hospital system can read directly.
L1
Sensing Hardware
Band01_Rev1 PCB · MAX30102 · MPU-6050 · MLX90632
Collects raw physiological data via I2C and SPI. The sensors measure heart rate, blood oxygen, body temperature, and 3-axis acceleration every 2 seconds. Data is passed to the onboard CC2640R2F microcontroller.
↓
L2
Firmware Processing
CC2640R2F · TI-RTOS · BLE GATT profile
The firmware reads sensor registers via I2C, applies calibration algorithms, and transmits the processed values via Bluetooth Low Energy (BLE) GATT profile. Currently the sensor reads are in development — placeholder values transmitted.
↓
L3
FHIR Gateway
Raspberry Pi 5 · Flask server · HL7 FHIR R4
The gateway receives BLE data and structures it as FHIR R4 Observation resources with proper LOINC codes and UCUM units. It exposes a REST API at /api/fhir/... — this is the layer that makes the device interoperable.
↓
L4
Clinical Consumers
Phone app · Doctor dashboard · Hospital EHR · Research platforms
Any FHIR-compatible system connects to the gateway REST API without custom integration. Epic, Cerner, OpenMRS, and research databases all speak FHIR R4 natively — enabling seamless data flow to wherever it is needed clinically.

## Slide 7
FHIR REST API — What the Gateway Exposes
Smartband V001 — FHIR Integration | HSHL | Masrur Jamil Prochchhod
The Raspberry Pi 5 gateway acts as a FHIR server. Any device or software that speaks HTTP can call these endpoints and receive properly structured FHIR R4 resources in return — no special driver or SDK required.
How the API Works
A client sends an HTTP GET request to an endpoint. The gateway reads the latest sensor data from the CSV log, wraps it in a FHIR resource with LOINC codes and UCUM units, and returns it as JSON. The client can be a phone app, a hospital EHR, or a research script — they all get the same standardized response.
GET
/api/fhir/patient
All registered patients — demographics, device, weight, height
GET
/api/fhir/observation
Complete snapshot — all current vital observations grouped together
GET
/api/fhir/observation/hr
Heart Rate (LOINC 8867-4) — beats per minute
GET
/api/fhir/observation/temp
Body Temperature (LOINC 8310-5) — degrees Celsius
GET
/api/fhir/observation/spo2
Blood Oxygen Saturation (LOINC 2708-6) — percentage
GET
/api/fhir/observation/steps
Step Count (LOINC 55423-8) — derived from MPU-6050 motion data
GET
/api/fhir/condition
Active health alerts — e.g. tachycardia episode, elevated temperature
GET
/api/fhir/careplan
Doctor's monitoring plan — thresholds, frequency, instructions

## Slide 8
Clinical Workflow — How Doctors Interact with Smartband FHIR Data
Smartband V001 — FHIR Integration | HSHL | Masrur Jamil Prochchhod
FHIR transforms the Smartband from a simple data collector into a clinical tool. The workflow below shows how a doctor can monitor a patient remotely, receive alerts, and document clinical decisions — all through the FHIR standard.
1
Patient wears Smartband V001
The device continuously collects HR, SpO2, body temperature, and acceleration every 2 seconds. The patient goes about their daily life wearing the band on the wrist.
↓
2
Bluetooth transmission to gateway
The CC2640R2F firmware transmits readings via BLE GATT profile to the Raspberry Pi 5 gateway. The Pmod BT2 module on the Pi receives the data via UART at 115200 baud.
↓
3
FHIR structuring at the gateway
The gateway maps raw sensor values to FHIR R4 Observation resources — adding LOINC codes, UCUM units, ISO 8601 timestamps, and a reference to the Patient resource.
4
Doctor accesses live FHIR data
The clinician opens the web app or their hospital EHR system. Both query the FHIR REST API and display live vitals, trend graphs, and the full alert history for each patient.
↓
5
Threshold crossed — alert generated
When HR exceeds 100 BPM, temperature exceeds 38.5°C, or acceleration exceeds 2.0G, a FHIR Condition resource is created and a FHIR Subscription pushes an alert to the doctor's device in real time.
↓
6
Doctor updates patient status
The doctor taps the patient card, changes status to 'Under Observation' or 'Critical', and types a clinical note. The note is stored as a FHIR Condition and visible immediately on all connected systems.

## Slide 9
Current PCB Sensors & Planned Future Hardware
Smartband V001 — FHIR Integration | HSHL | Masrur Jamil Prochchhod
Band01_Rev1 already carries three sensors whose FHIR mapping is defined and ready. Five additional sensors are planned for future PCB revisions to expand clinical coverage — each with a specific recommended module for procurement.
Already on Band01_Rev1 PCB
MAX30102
Heart Rate & SpO2
Optical sensor using 660nm red and 940nm IR LEDs. Detects blood flow through the wrist to calculate HR (LOINC 8867-4) and blood oxygen saturation (LOINC 2708-6). Interface: I2C at address 0x57.
MPU-6050
Accelerometer & Gyroscope
6-axis IMU with ±16g accelerometer and ±2000°/s gyroscope. Provides raw motion data for step counting (LOINC 55423-8), fall detection, and activity classification. Interface: I2C at 0x68.
MLX90632
Infrared Temperature
Non-contact IR thermometer measuring skin surface temperature to ±0.2°C accuracy. Calculates core body temperature via built-in DSP algorithm. FHIR: LOINC 8310-5. Interface: I2C at 0x3A.
Planned Future Hardware
AD8232
ECG
SparkFun DEV-12650. Single-lead ECG front-end. Detects arrhythmia and atrial fibrillation. LOINC 11524-6. Needs 2–3 skin electrodes.
Grove GSR
Stress / EDA
Seeed Studio SKU 101020052. Measures skin conductance for stress monitoring. LOINC 74767-6. Analog ADC interface.
ProtoCentral BP2
Blood Pressure
PPG-based wrist BP estimation. Systolic/Diastolic pressure. LOINC 55284-4. mm[Hg] units. High clinical demand.
TI AFE4490
Blood Glucose
Near-infrared optical front-end for non-invasive glucose monitoring. LOINC 15074-8. mmol/L. Emerging technology.
ICM-42688-P
Respiratory Rate
TDK InvenSense high-precision IMU. Breathing rate derived from motion. LOINC 9279-1. /min. Can also be derived from MAX30102 PPG signal.

## Slide 10
Five-Phase FHIR Implementation Roadmap
Smartband V001 — FHIR Integration | HSHL | Masrur Jamil Prochchhod
FHIR integration is built incrementally — each phase delivers real clinical value while setting up the next. Phase 1 is already underway. The roadmap is designed so the professor and project team can clearly see what comes next and why.
Phase 1
Foundation
FHIR Patient + Observation resources with LOINC coding
Flask REST API exposing /api/fhir/ endpoints
Phone web app showing live vitals + FHIR tab
Simulated sensor data as placeholder
Current
→
Phase 2
Real Sensor Data
Activate commented-out sensor reads in i2c_sensors.c
Replace 0x7788 placeholder with real MAX30102/MPU-6050 values
Real HR, SpO2, temperature, acceleration via BLE
Calibration and validation of sensor outputs
Next
→
Phase 3
Clinical Workflow
FHIR Condition, CarePlan, Practitioner resources
Full doctor dashboard with FHIR backend
FHIR Subscription — real-time alert push to doctor
SMART on FHIR OAuth 2.0 authentication
Phase 3
→
Phase 4
EHR Integration
Deploy HAPI FHIR open-source server
Validate against official HL7 FHIR validator
Connect to hospital EHR test environment (Epic/Cerner)
FHIR AuditEvent logging for GDPR compliance
Phase 4
→
Phase 5
Certification
EU MDR 2017/745 device classification review
GDPR data protection impact assessment
ISO 13485 quality management evaluation
HL7 FHIR conformance testing and certification
Phase 5

## Slide 11
Data Privacy, GDPR Compliance & SMART on FHIR Authentication
Smartband V001 — FHIR Integration | HSHL | Masrur Jamil Prochchhod
Health data is the most sensitive category of personal data under GDPR. The Smartband V001 FHIR implementation must address privacy from the ground up — not as an afterthought. SMART on FHIR provides the industry-standard authentication layer.
GDPR & Regulatory Compliance
Encryption in transit
All FHIR API calls use HTTPS/TLS. Data in transit is never readable even if intercepted on the network. Mandatory under GDPR Article 32.
Encryption at rest
All patient data stored on the server is encrypted. The database itself is inaccessible without the decryption key. Required by GDPR Article 32.
Patient consent (Art. 7)
Every patient must give explicit consent before data collection begins. Consent is stored as a FHIR Consent resource and can be withdrawn at any time.
Right to erasure (Art. 17)
Patients can request deletion of all their health data. The FHIR DELETE operation removes all Observations, Conditions, and Patient resources permanently.
Audit logging
Every access and modification is logged as a FHIR AuditEvent resource. This creates a tamper-proof compliance trail required by ISO 27001 and HIPAA.
EU MDR 2017/745
The device must be classified under the EU Medical Device Regulation. FHIR compliance is increasingly considered during conformity assessment.
SMART on FHIR — OAuth 2.0 Auth Layer
SMART on FHIR is the authorization framework built on top of FHIR. It uses OAuth 2.0 tokens to control who can access which patient data. Without valid credentials, the FHIR API returns a 401 Unauthorized error — no data is exposed.
Doctor login
Receives a scoped token — can only see their assigned patients. Cannot access other doctors' patient lists.
Patient login
Receives a narrower token — read-only access to their own observations and care plan. Cannot modify records.
Research app
Requests anonymized, aggregated data only. Individual patient identifiers are never included in the response.
Token security
All endpoints require a valid OAuth 2.0 bearer token in the HTTP header. Tokens expire after a configurable period.

## Slide 12
FHIR Server Options — Moving Beyond the Prototype
Smartband V001 — FHIR Integration | HSHL | Masrur Jamil Prochchhod
The current Flask implementation is a prototype. For production deployment — or even a serious academic demonstration — a dedicated FHIR server is required. The recommended option for this project is HAPI FHIR due to its open-source nature and full R4 compliance.
Why a dedicated FHIR server?
The Flask server is a custom implementation — it produces FHIR-shaped JSON but does not perform full FHIR validation, does not support FHIR search parameters, and does not implement the FHIR capability statement. A proper FHIR server handles all of this automatically and passes the official HL7 conformance tests.
HAPI FHIR
Open source Java · Free
The most widely used open-source FHIR server. Runs locally on a Pi or cloud VM. Full R4 compliance, built-in FHIR validator, and REST API. Recommended for this project.
★ Pick
Azure Health Data
Cloud FHIR service · Pay per use
Microsoft Azure's managed FHIR service. No server maintenance required. Integrates with Azure Logic Apps for automated workflows. Suitable for production cloud deployment.
AWS HealthLake
Cloud FHIR service · Pay per use
Amazon's FHIR-native health data lake. Includes built-in ML capabilities for predictive analytics. Best for large-scale research data aggregation across many devices.
Google Cloud FHIR
Cloud FHIR service · Pay per use
Google Cloud Healthcare API with FHIR R4 support. Integrates with BigQuery for advanced analytics. Best for research institutions already using Google Cloud infrastructure.
OpenMRS FHIR
Open source · Free
Open-source EHR with built-in FHIR module. Ideal for connecting Smartband data directly into a running EHR instance for academic demonstration purposes at HSHL.

## Slide 13
Next Steps & Recommendations — Action Plan
Smartband V001 — FHIR Integration | HSHL | Masrur Jamil Prochchhod
These seven actions, taken in order, will transform the Smartband V001 from a prototype demonstration into a clinically meaningful, FHIR-compliant health monitoring device.
1
Activate firmware sensor reads
Uncomment the sensor reading calls in i2c_sensors.c on the CC2640R2F firmware. Replace the 0x7788 placeholder value with real MAX30102, MPU-6050, and MLX90632 readings transmitted via BLE GATT.
2
Procure future sensors
Order: AD8232 ECG module (SparkFun DEV-12650), Grove GSR Sensor v1.2 (Seeed SKU 101020052), ProtoCentral BP2 blood pressure module. These three expand clinical coverage the most at lowest cost.
3
Expand the FHIR API
Add FHIR Condition resources for alert events, SpO2 Observation endpoint, and a /api/fhir/observation/history endpoint returning the last N readings as a FHIR Bundle with proper timestamps.
4
Deploy HAPI FHIR server
Install HAPI FHIR on the Raspberry Pi or a cloud VM. Migrate data storage from CSV to the HAPI FHIR database. This enables full FHIR search, validation, and capability statement support.
5
Implement SMART on FHIR authentication
Add OAuth 2.0 login to the web app and API. Use Keycloak or a similar identity provider. Role-based scopes — doctor vs patient — control what each user can see and modify.
6
FHIR Subscription for real-time alerts
Register FHIR Subscriptions so the doctor's phone receives a push notification the moment a patient's HR exceeds 100 BPM, temperature exceeds 38.5°C, or a fall is detected via acceleration.
7
FHIR conformance testing & EU MDR review
Run the official HL7 FHIR validator against all API endpoints. Commission an EU MDR 2017/745 device classification review to determine whether medical device certification applies.

## Slide 14
The Bigger Picture — Why This Matters for Healthcare
Smartband V001 — FHIR Integration | HSHL | Masrur Jamil Prochchhod
FHIR is not just a technical standard — it is the infrastructure that makes personalized, data-driven medicine possible. The Smartband V001 project positions itself at the intersection of wearable IoT and clinical-grade health IT.
From Prototype to Clinical Tool
Today, the Smartband V001 is a student prototype — it collects simulated data and sends it to a phone app. With FHIR integration, the exact same hardware becomes a clinical-grade remote patient monitoring device whose data is readable by every hospital system in the world. The code and architecture described in this presentation are the bridge between those two realities.
Teaching Value of This Project
This project demonstrates in a single system: embedded firmware development (CC2640R2F), wireless communication (BLE), IoT gateway design (Raspberry Pi), RESTful API development (Flask), international health IT standards (FHIR R4, LOINC, UCUM), data privacy law (GDPR), and medical device regulation (EU MDR). It is a complete vertical slice of modern connected health.
168+
countries use LOINC codes
FHIR R4
required by US ONC & EU MDR
Epic · Cerner
both use FHIR R4 natively
0 custom code
needed for EHR integration
5 sensors
already on Band01_Rev1 PCB
18 references
in the FHIR prospects report

## Slide 15
Thank You
Smartband V001 — FHIR Integration Prospects
✦ HL7 FHIR R4 — The international standard — 168+ countries, required by Epic, Cerner, EU MDR, and US FDA
✦ LOINC + UCUM — Every sensor reading carries a universally understood code and unit — no ambiguity across systems
✦ 4-Layer Architecture — Hardware → Firmware → FHIR Gateway → Clinical Consumers — each layer clearly separated
✦ 5-Phase Roadmap — From current prototype to certified, EHR-integrated, GDPR-compliant clinical device
✦ 18 Academic References — Grounded in peer-reviewed literature — Pinheiro et al. (2022) and HL7 FHIR specification
Masrur Jamil Prochchhod · Hochschule Hamm-Lippstadt (HSHL) · June 2026
Submitted to: Prof. Dr. Javidi da Costa, Joao Paulo