## Slide 1
Smartband V001 — Rev1
CCS 21 Migration & Debug Session
Masrur Jamil Prochchhod · Hochschule Hamm-Lippstadt · Prof. Giovanni

## Slide 2
BACKGROUND
Why CCS 12.8.1 → CCS 21
The trigger
CCS 12.8.1 stopped enumerating the onboard XDS110 debug probe — Windows “Code 28” driver error, unresolvable within the existing install.
The response
Installed CCS 21 as a fresh, separate toolchain — reusing the existing SDK 5.30.1.11, and manually adding the classic ti-cgt-arm 20.2.7.LTS compiler (CCS 21 defaults to TI ARM Clang, incompatible with this SDK).
CCS 21 (Wireless Connectivity)
ti-cgt-arm 20.2.7.LTS (manual)
SDK 5.30.1.11 (reused)
XDCtools 3.51.3.28 (reused)
2

## Slide 3
BUILD SYSTEM
Ten Independent Build Blockers
CCS 21’s project generator did not reproduce CCS 12.8.1’s working configuration. Each issue below masked the next until resolved, in order encountered:
1
Wrong active build config repeatedly edited (FlashROM_Library_PTM, not the active FlashROM_Library)
2
Missing workspace-level SDK path variable → “69 unresolved linked resources”
3
Missing XDCtools packages include path → intermittent xdc/std.h errors
4
Missing / duplicated NPI include path across two SDK trees
5
osal_cbtimer.c & rom_init.c needed explicit exclusion from build
6
C89 vs. C99 mismatch — required enabling --c99
7
Stale macro name in vendor source (mb_patch.c) — patched directly
8
Missing USE_ICALL / ICALL_LITE / STACK_LIBRARY predefines
9
Linker library list stripped to just libc.a — rebuilt from scratch
10
Outer/inner duplicate-named project folders confusing the importer
3

## Slide 4
ROOT CAUSE SPOTLIGHT
The STACK_LIBRARY Define
The single fix with the widest blast radius
icall_api_idx.h branches on #ifndef STACK_LIBRARY. Without that define, the app pulled in ble_dispatch_lite_idx.h — an unfinished code-generation template, not real firmware.
Symptom
Gap_RegisterConnEventCb and MAX_NUM_BLE_CONNS came back “undefined” — looked like a missing include, was actually a missing #define.
Fix
Add STACK_LIBRARY alongside USE_ICALL and ICALL_LITE in the app project’s predefined symbols — all three must be present together.
Predefined Symbols (app project)
DeviceFamily_CC26X0R2
CC2640R2_LAUNCHXL
ICALL_JT
ICALL_EVENTS
ICALL_STACK0_ADDR
USE_ICALL
ICALL_LITE
STACK_LIBRARY
4

## Slide 5
ROOT CAUSE SPOTLIGHT
The Evidence, in Code
icall_api_idx.h — the branch that decided everything
#ifndef STACK_LIBRARY
#include "ble_dispatch_lite_idx.h" // <<INSERT:...>> template, incomplete
#else
// ... real, populated #define IDX_Gap_RegisterConnEventCb ...
#endif
Without STACK_LIBRARY, the app silently took the template branch — producing “undefined identifier” errors that looked like a missing #include, not a missing #define.
mb_patch.c — a stale macro name from an out-of-sync SDK header
error #20: identifier "INT_RFC_CPE1" is undefined
error #20: identifier "INT_RFC_CPE0" is undefined
hw_ints.h (current driverlib):
#define INT_RFC_CPE_1 18
#define INT_RFC_CPE_0 25
5

## Slide 6
DEBUG ACCESS
XDS110 Connection Recovery
1
Error -242
Router subpath inaccessible — wiring, jumper and probe firmware all ruled out
2
Error -2131 / -241
Register access failure → SC_ERR_ROUTER_SECURE_SUBPATH — CC2640R2F debug interface is CCFG-locked
3
UniFlash: Force Mass Erase
Settings & Utilities → Erase Entire Flash — clears the CCFG lock
4
CCS 21 connects normally
Flash and debug restored; board runs and advertises correctly
6

## Slide 7
VALIDATION
What’s Confirmed Working
✓
BLE Stack
Advertises as “Simple Peripheral”, connects in nRF Connect
✓
OLED Display
SSD1306 renders sensor data correctly (debugger attached)
✓
I2C Sensors
LIS331, MAX30102, MAX30205 all read correctly
✓
Build & Flash
Clean build → flash → run cycle fully functional under CCS 21
7

## Slide 8
OPEN ISSUE
Standalone Cold-Boot Power Loss
With the LaunchPad disconnected, cycling the PeakTech bench supply causes the board to lose power entirely rather than reboot.
Passive components checked — all measured correctly
Check | Expected | Result
I2C SCL pull-up (R103) → 3V3 | ~10 kΩ | ✓ OK
I2C SDA pull-up (R104) → 3V3 | ~10 kΩ | 9.92 kΩ – OK
nRESET pull-up (R1) → 3V3 | ~100 kΩ | 98.8 kΩ – OK
JTAG TDI/TDO pulls (R17/R18, DNM) | Open | ✓ OK
I2C0 pin map in firmware (SCL=IOID_5, SDA=IOID_6) | Matches Rev1 | ✓ OK
8

## Slide 9
NEXT STEPS
Where We Pick Up
1
Continuity check (board unpowered): P10 Extern-Pwr side → P1 pin 16 (VBAT)
2
Visual inspection of the P10 header for a cold solder joint or bent pin
3
Repeat standalone-boot test on LiPo + TP4056 once battery arrives — isolates PeakTech current-limit behaviour as a factor
9

## Slide 10
CCS 21 migration: complete.
Build, flash, debug, BLE and sensors all confirmed working.
One open hardware item remains: standalone cold-boot power.