## Slide 1
SMARTBAND V001 REV2
Full System Development Report
Dashboards · Cloud · Hospital Portal · FHIR · Registration · Recommendations
Student:
Masrur Jamil Prochchhod
Matric:
2210028
Institution:
Hochschule Hamm-Lippstadt (HSHL)
Supervisor:
Prof. Giovanni (giovannix)
Platform:
Raspberry Pi 5 · Flask · Firebase
Date:
June 2026

## Slide 2
What We Built — Overview
Six dashboards · Cloud storage · 20+ API endpoints · 7 Python modules
📱
Main Dashboard
AMOLED patient UI · ECG · 16 sensors · live charts
👨‍⚕️
Doctor Dashboard
Multi-patient · threshold alerts · recommendations
🏥
Hospital Portal
Band management · allocation · patient monitoring
🔬
FHIR R4 Lab
8 LOINC codes · searchset bundle · all patients
📋
Patient Register
Band ID system · SB-XXXXXX · doctor search
☁️
Firebase Cloud
Patients · readings · alerts · registered — 4 collections
7
Python modules
13
HTML templates
20+
API endpoints
5
Patients live
8
LOINC codes
4
Cloud collections

## Slide 3
Main Dashboard — Patient Interface
http://192.168.0.110:5000/ · Live ECG · 16 sensors · scenario switcher · recommendations
● SMARTBAND 192.168.0.110:5000
ECG ⚡ 75 BPM
75
HR BPM
98
SpO₂ %
36.6
Temp °C
45
HRV ms
118/76
BP mmHg
28
Stress %
15
RR /min
0
Floor lvl
Scenarios: Normal Workout Fever Fall Sleep Stairs
🏥 Hospital 📋 Register 👨‍⚕️ Doctor 📊 FHIR
📩 Doctor recommendations — 2 new
Key Features
🫀 Live ECG strip
Synthesised PQRST via Gaussian maths · green canvas glow · 64 samples at 256Hz
📊 16 sensor channels
HR · SpO2 · Temp · HRV · BP · Stress · RR · Floor · Steps · Calories · Sleep · Battery
🎯 Scenario switcher
6 scenarios change all 16 channels simultaneously — Normal/Workout/Fever/Fall/Sleep/Stairs
📈 Trend charts
4 Chart.js sparklines — HR, SpO2, Temp, Acceleration — live updating every 2s
👤 Patient profile
Name, DOB, weight, height, city — feeds into FHIR Patient resource
💜 Recommendations
Doctor messages with urgency — unread dot — mark as read — 10s auto-refresh
🆔 My Band ID
Shows SB- registration code · Copy button · persists in localStorage

## Slide 4
Doctor Dashboard — Clinical Multi-Patient View
http://192.168.0.110:5000/doctor · 5 patients · threshold alerts · recommendations · FHIR
🚨 Active patient alerts 3 alerts Dismiss
MJ
Masrur Jamil
24 yrs · normal
OK
75
HR
98%
SpO2
36.6°
Temp
118/76
BP
AS
Anna Schmidt
67 yrs · hypertension
ALERT
84
HR
97%
SpO2
36.5°
Temp
168/104
BP
⚠ Threshold alert active
HW
Hans Weber
45 yrs · fever
!!EMG
108
HR
95%
SpO2
39.4°
Temp
128/82
BP
⚠ Threshold alert active
MM
Maria Müller
33 yrs · normal
OK
72
HR
99%
SpO2
36.6°
Temp
112/70
BP
KF
Klaus Fischer
72 yrs · copd
ALERT
88
HR
86%
SpO2
36.4°
Temp
138/85
BP
⚠ Threshold alert active

## Slide 5
Patient Registration — Band ID System
http://192.168.0.110:5000/register · Unique SB- IDs · doctor search · localStorage persistence
Patient Registration Flow
1
Patient opens /register
From main dashboard nav — "Register my band" button
2
Fills in profile form
Name, DOB, gender, weight, height, city, medical notes
3
Submits — Band ID generated
Server creates unique SB-XXXXXX (6-char alphanumeric)
4
Profile saved
registered_patients.json + Firebase Firestore registered/
5
Patient sees their Band ID
Shown prominently with Copy button and step instructions
6
ID saved to localStorage
Shows on main dashboard "My Band ID" card on return visits
7
Patient gives ID to doctor
Doctor types ID in search box on doctor dashboard
8
Doctor adds patient
Profile auto-fills — doctor picks scenario — one click add
Your Band ID
SB-4K2M9
Share this ID with your doctor
1 Write down or screenshot your Band ID
2 Give it to your doctor at your next visit
3 Doctor searches by ID — your data auto-fills
Doctor adds patient — Band ID search
SB-4K2M9
Masrur Jamil
24 yrs · male · Hamm
SB-4K2M9

## Slide 6
Hospital Portal — Band Management
http://192.168.0.110:5000/hospital/register · Band inventory · allocation · release · monitoring
Hospital Registration
Hospital name
St. Marien Hospital
City
Hamm
Contact person
Dr. Schmidt
Bands to register
10
PIN
••••••
Generated ID
HOSP-AB1234
Band Inventory Dashboard
10
TOTAL
4
AVAIL
3
ALLOC
3
IN USE
001
AVAILABLE
Allocate
002
AVAILABLE
Allocate
003
ALLOCATED
Anna Schmidt
Release
004
IN USE
Hans Weber
Release
005
ALLOCATED
Klaus Fischer
Release
006
IN USE
Maria Müller
Release
Band lifecycle: Available → Allocated → In Use → Released → Available

## Slide 7
FHIR R4 + Firebase Firestore Cloud
Clinical data standards · 8 LOINC codes · 4 Firestore collections · auto-sync every 30s
FHIR R4 — 8 Clinical Observations
8867-4
Heart rate
/min
2708-6
Oxygen saturation
%
8310-5
Body temperature
Cel
9279-1
Respiratory rate
/min
55284-4
Systolic BP
mm[Hg]
8462-4
Diastolic BP
mm[Hg]
74767-6
Stress / EDA
%
80404-7
HRV
ms
Steps and calories removed — not clinical observations
Firebase Firestore — Cloud Storage
Project: smartband-hshl-5b91d · Region: europe-west3
patients/
{pid}
Full profile · name, age, gender, condition
sensor_readings/
{pid}/readings/auto
All vitals every 30s · rate-limited for free tier
alerts/
{auto-id}
Threshold violations · on state change only
registered/
{band_id}
Self-registered patients · Band IDs
Daily write budget (free tier: 20,000)
14,400 used / 20,000 limit (72%)

## Slide 8
Doctor Recommendations + Health Summary
Doctor-to-patient messaging · urgency levels · Health Summary trends and goals
Doctor Recommendations System
DOCTOR SIDE
📝 button on each patient card
✓ Routine
⚠ Important
🚨 Urgent
Increase fluid intake. Monitor BP daily.
Send recommendation
PATIENT SIDE — main dashboard
● New
Increase fluid intake. Monitor BP daily. — Dr. Schmidt · Urgent
Refreshes every 10s · click to mark as read · urgency colour-coded
Health Summary — /summary
All time
11 Jun
10 Jun
09 Jun
Goal Progress Rings
92%
Resting HR
98%
SpO2 Goal
74%
Readings
74 BPM
Avg HR
97.8%
Avg SpO2
36.8°C
Max Temp
28%
Avg Stress
4 trend charts: HR · SpO2 · Temp · Acceleration · Full session log table

## Slide 9
System Architecture — How Everything Connects
Flask · Simulator · Cloud · Dashboards · Data flow
Browser / Client
· index.html (patient)
· doctor.html (clinical)
· hospital_dashboard.html
· fhir_view.html
· register.html
· summary.html
↕
Flask Application
· app.py — 20+ routes
· Page routes + API endpoints
· Error handling + logging
· FHIR bundle builder
↕
Core Python Modules
· simulator.py — 5 patients 16ch
· hospital_storage.py — bands+recs
· cloud_storage.py — Firebase sync
· drivers.py — OLED
↕
Storage Layer
· data/*.json (local)
· Firebase Firestore (cloud)
· sensor_data.csv (history)

## Slide 10
Next Steps — What Comes After This Session
Hardware · Firmware · Mobile App · PCB Design · Clinical Validation
Phase 1 — ORDER NOW
nRF5340 DK development kit (~€45) from mouser.de
J-Link EDU Mini debug probe (~€22) from shop.segger.com
Waveshare 1.69" Touch LCD (~€20) from waveshare.com
Install nRF Connect SDK v2.6.1 on Windows
Phase 2 — FIRMWARE
Zephyr RTOS bringup on nRF5340 DK
Sensor drivers: ICM-42688-P → BMP390L → MAX30102 → MLX90632 → MAX30001
BLE GATT service with all 16 sensor channels
OLED display via LVGL on ST7789V2
Phase 3 — SOFTWARE
BLE client in Python (bleak) — real sensor data into Flask
Replace simulator.py with live BLE readings
SQLite migration — replace JSON files with proper database
Flask-Login user authentication
Phase 4 — PCB + VALIDATION
KiCad schematic from BOM — all 42 components
4-layer PCB layout — RF keepout, analog isolation
JLCPCB fabrication with PCBA service
Clinical validation vs Contec CMS50D+ and Omron M3

## Slide 11
Session Complete
Everything built in this session is live and running on the Raspberry Pi
7
Python modules
simulator · drivers · cloud · hospital · app · settings · config
6
Dashboards
Main · Doctor · Hospital · FHIR · Register · Summary
5
Live patients
Each with own scenario · vitals · alerts · FHIR bundle
4
Cloud collections
patients · sensor_readings · alerts · registered
8
LOINC codes
Full FHIR R4 clinical observations — no steps/calories
20+
API endpoints
Pages + data APIs + FHIR + hospital + cloud
Masrur Jamil Prochchhod · 2210028 · HSHL · Prof. Giovanni (giovannix) · June 2026