## Slide 1
FIRMWARE BUILD
ENVIRONMENT ISSUES
& RESOLUTIONS REPORT
Band01_Rev1 Smartband · Task 3 Development Log
Prepared by: Masrur Jamil Prochchhod Matriculation: 2210028 Environment: CCS v12.8.1 · TI CC2640R2 SDK v5.30.01.11 · Windows 11 Date: 28 May 2026
HSHL Internship Project · June 2026

## Slide 2
BUILD ENVIRONMENT — Context & Overview
Project Context
Target: CC2640R2FRSMR BLE SoC (Smartband V001) Tool: Code Composer Studio v12.8.1 SDK: TI SimpleLink CC2640R2 SDK v5.30.01.11 App workspace: workspace_v12 Stack workspace: workspace_v13 Goal: Get the firmware to compile and link on a fresh machine
3 Issues — All Resolved
1
Missing build_config.opt
All 25+ source files failed — compiler options file absent from repo
2
Missing BLE Stack Library
Linker could not find the 3 required binary stack files
3
Header Mismatch gapbondmgr.h
Header declared 2 functions differently from compiled library
✓ All 3 issues resolved · 0 errors · Build completed 28 May 2026
Firmware Build Environment Report · Band01_Rev1 · Task 3 · Masrur · HSHL 2026

## Slide 3
ISSUE 1 — Missing build_config.opt
✓ RESOLVED
Error
Cannot open command file
'/TOOLS/build_config.opt'
No such file or directory
Repeated for ALL 25+ source files.
Secondary error:
#error "RF_SINGLEMODE
missing" at line 64 of
RFCC26XX_singleMode.c
Root Cause
CCS project references:
--cmd-file="${REF_PROJECT_1_LOC}
/TOOLS/build_config.opt"
REF_PROJECT_1_LOC pointed to the stack project folder — never committed to GitHub.
On a fresh machine this resolves to /TOOLS/... — a path that doesn't exist.
Resolution
Manually created:
C:\TOOLS\build_config.opt
With 8 required preprocessor flags:
-DRF_SINGLEMODE
-DUSE_ICALL
-DICALL_LITE
-DPOWER_SAVING
-DHEAPMGR_SIZE=0
-DMAX_NUM_BLE_CONNS=1
...
Committed to repo at
TOOLS/build_config.opt
Firmware Build Environment Report · Band01_Rev1 · Task 3 · Masrur · HSHL 2026

## Slide 4
ISSUE 2 — Missing BLE Stack Library
✓ RESOLVED
Linker Errors:
#10008-D cannot find "/FlashROM_Library/.lib"
#10008-D cannot find "/FlashROM_Library/ble_r2.symbols"
#10008-D cannot find "/FlashROM_Library/lib_linker.cmd"
#10192 Failed linktime optimization
symbol "RF_cancelCmd" redeclared... (15+ more)
Root Cause:
The 3 files are compiled outputs of the BLE stack library project (smart_band_v001_stack_library) — never committed to repo (binary files).
First attempt used BLE5 stack by mistake → 20+ new symbol conflicts. Correct stack: blestack (BLE4), not ble5stack.
Resolution — 3 Files Required:
.lib
Stack library binary
→ C:\FlashROM_Library\.lib
lib_linker.cmd
Linker command file
→ C:\FlashROM_Library\
lib_linker.cmd
ble_r2.symbols
Symbol export table
→ C:\FlashROM_Library\
ble_r2.symbols
⚠ These are binary files — cannot be committed to the repo.
Every new developer must build the BLE4 stack library from SDK blestack examples and copy the 3 files to C:\FlashROM_Library\
Firmware Build Environment Report · Band01_Rev1 · Task 3 · Masrur · HSHL 2026

## Slide 5
ISSUE 3 — gapbondmgr.h Header Mismatch
✓ RESOLVED
Final Linker Errors:
symbol "GAPBondMgr_PasscodeRsp" redeclared with incompatible type: smart_band_v001_app
symbol "GAPBondMgr_Register" redeclared with incompatible type: smart_band_v001_app
#10192 Failed linktime optimization
The Problem — Header vs Library Version Mismatch:
Include/gapbondmgr.h (repo copy)
OLD version — declares GAPBondMgr_PasscodeRsp and GAPBondMgr_Register with outdated parameter types
≠
Compiled .lib (from current SDK)
NEW version — same functions compiled with updated signatures. Linker detects conflict and refuses to link.
Resolution:
Replaced Include/gapbondmgr.h with the correct version from: C:\ti\simplelink_cc2640r2_sdk_5_30_01_11\source\ti\blestack\profiles\roles\gapbondmgr.h
File committed back to repository so future developers get the correct header on clone.
Firmware Build Environment Report · Band01_Rev1 · Task 3 · Masrur · HSHL 2026

## Slide 6
FINAL BUILD RESULT — 0 Errors
✓ smart_band_v001_app — BUILD SUCCESSFUL — 0 Errors — 28 May 2026
All 3 issues resolved in sequence · Output files generated · Ready to flash via JTAG
Output Files Generated:
smart_band_v001_app.out
ELF Binary
Used by CCS debugger for flashing and step-through debugging via JTAG probe
smart_band_v001_app.hex
Intel HEX
Used for direct flashing tools — stored in repository from original build
smart_band_v001_app.map
Linker Map
Shows exact Flash and RAM memory usage for every compiled module
Firmware state: Sensor calls are currently commented out — transmits placeholder value 0x7788 via BLE GATT. Ready to flash once JTAG probe and power supply are connected.
Firmware Build Environment Report · Band01_Rev1 · Task 3 · Masrur · HSHL 2026

## Slide 7
FUTURE DEVELOPER SETUP GUIDE
1
Clone repository
TOOLS/build_config.opt and Include/gapbondmgr.h are now present — no manual recreation needed
2
Install TI SDK
TI SimpleLink CC2640R2 SDK v5.30.01.11 required at C:\ti\simplelink_cc2640r2_sdk_5_30_01_11\
3
Import & build stack library
Import simple_peripheral_cc2640r2lp_stack_library from blestack SDK examples into a separate workspace (workspace_v13)
4
Copy 3 output files
Copy .lib, lib_linker.cmd, ble_r2.symbols from build output to C:\FlashROM_Library\
5
Build app project
Import smart_band_v001_app into workspace_v12 and build — should complete with 0 errors
6
Flash via JTAG
Connect XDS110 debug probe, power the board, use CCS to flash smart_band_v001_app.out
Firmware Build Environment Report · Band01_Rev1 · Task 3 · Masrur · HSHL 2026

## Slide 8
SUMMARY
Issue 1
build_config.opt was absent from the repo — created and committed
Issue 2
BLE4 stack library missing — built from SDK blestack examples, placed at C:\FlashROM\
Issue 3
gapbondmgr.h out of sync with SDK — replaced with correct version and committed
Result
0 errors · Build completed 28 May 2026 · .out, .hex, .map files generated
Firmware
Transmits placeholder 0x7788 via BLE GATT — ready to flash once JTAG probe available
Band01_Rev1 Smartband · Task 3 · Masrur Jamil Prochchhod · Matriculation: 2210028 · HSHL 2026