## Slide 1
SMARTBAND V001
Hardware Integration &
System Demonstration Report
Task 3 — Peripheral Integration Phase · Raspberry Pi 5
Student: Masrur Institution: Hochschule Hamm-Lippstadt (HSHL) Repository: Band01_Rev1 (Private GitHub) Date: June 2026
Objective: Establish complete end-to-end health monitoring pipeline — BT, OLED, LED, buzzer, live plot, ThingsBoard cloud
HSHL Internship Project · June 2026

## Slide 2
HARDWARE COMPONENTS
Component
Type
Interface
GPIO / Address
Raspberry Pi 5
Host Platform
—
—
Pmod BT2 (RN-42)
Bluetooth Module
UART
GPIO14 (TX), GPIO15 (RX)
SSD1306 128×64
OLED Display
I2C
0x3C · SDA: GPIO2, SCL: GPIO3
RGB LED
Common Cathode
GPIO
Red: GPIO27 · Green: GPIO26
Active Buzzer
Alarm Module
GPIO
GPIO17
T-Shaped Extension Board
GPIO Extender
Ribbon Cable
40-pin breakout
Smartband V001 · Hardware Integration & System Demonstration · Task 3 · HSHL 2026

## Slide 3
WIRING & PIN MAPPING
OLED SSD1306 (I2C)
VCC
3V3 (left)
e5
GND
GND (left)
e9
SDA
SDA1 (left)
e6
SCL
SCL1 (left)
e7
Pmod BT2 Bluetooth (UART)
Pin 2 (RX)
TXD0 (right)
f8
Pin 3 (TX)
RXD0 (right)
f9
Pin 5 (GND)
GND (right)
i21
Pin 6 (VCC)
3V3 (left)
e13
RGB LED & Buzzer (GPIO)
Component
GPIO
Ext. Label
Breadboard
RGB LED Red
GPIO27
GPIO27
a40 via 330Ω
RGB LED Green
GPIO26
GPIO26
a42 via 330Ω
RGB LED GND
GND
GND
a41
Buzzer (+)
GPIO17
GPIO17
a30
Buzzer (−)
GND
GND
a34
Smartband V001 · Hardware Integration & System Demonstration · Task 3 · HSHL 2026

## Slide 4
SOFTWARE ARCHITECTURE & DATA PIPELINE
System Files:
smartband_full_v3.py
Main system — sensor simulation, OLED, LED, buzzer, BT, ThingsBoard, CSV
smartband_plot.py
Real-time matplotlib dashboard — reads sensor_data.csv and plots live graphs
font5x8.bin
Bitmap font required by adafruit_ssd1306 for OLED text rendering
Data Flow (every 2 seconds):
Sensor Simulator
HR · Temp · Accel
sensor_data.csv
→ live_plot.py
ThingsBoard MQTT
mqtt.eu.thingsboard
Pmod BT2 UART
→ Android SPP
OLED SSD1306
HR / T / A display
RGB LED + Buzzer
Emergency alert
Emergency Logic
• Heart Rate > 100 BPM
→ Red LED flash + Buzzer ON + OLED emergency screen
• Temperature > 38.5°C
→ Red LED flash + Buzzer ON + OLED emergency screen
• Acceleration > 2.0 G
→ Red LED flash + Buzzer ON + OLED emergency screen
Smartband V001 · Hardware Integration & System Demonstration · Task 3 · HSHL 2026

## Slide 5
BLUETOOTH INTEGRATION — Pmod BT2 (RN-42)
Module Details:
Chip
Microchip RN-42
Device Name
RNBT-0793
MAC Address
00:06:66:F9:07:93
Baud Rate
115200 bps, 8N1
Profile
Classic Bluetooth SPP
Mode
Slave (waits for incoming)
Auth
Disabled (SA,0) — open pairing
UART Device
/dev/serial0
Connection Method (v3)
Pi UART (/dev/serial0) → Pmod BT2 → Wireless SPP to Android.
Eliminates rfcomm dependency. Any Android device can connect directly to RNBT-0793 and receive live sensor data via Serial Bluetooth Terminal app.
Android Data Format (Verified ✓)
HR:75 T:36.6 A:1.2
!! EMERGENCY !! HR:115 T:39.2 A:2.8
✓ Android verification: Paired with RNBT-0793 via Serial Bluetooth Terminal — live data stream confirmed
Smartband V001 · Hardware Integration & System Demonstration · Task 3 · HSHL 2026

## Slide 6
OLED DISPLAY & THINGSBOARD CLOUD
SSD1306 Display Screens:
Sensor View
HR, Temp, Accel, Timestamp
Normal — alternates every 2s
Status View
Date, Time, ThingsBoard status
Normal — alternates every 2s
Emergency View
!! EMERGENCY !!, all sensor values
Any threshold exceeded
Startup Screen
Smartband V001, HSHL Project, Starting...
System boot
Shutdown Screen
System OFF, Goodbye!, HSHL Project
Keyboard interrupt
ThingsBoard Cloud (MQTT)
Host:
mqtt.eu.thingsboard.cloud
Port:
1883
Protocol:
MQTT (paho-mqtt v2)
Topic:
v1/devices/me/telemetry
Fields:
heartRate, temperature, acceleration,
status, hr_limit, temp_limit, acc_limit
Offline:
Graceful — all local ops continue
(OLED, LED, buzzer, CSV, BT)
Smartband V001 · Hardware Integration & System Demonstration · Task 3 · HSHL 2026

## Slide 7
TESTING & VERIFICATION — 14 Tests All Passed
✓
OLED Detection
i2cdetect -y 1
0x3C detected
✓
OLED Display
adafruit_ssd1306 text render
Text displayed correctly
✓
Pmod BT2 Power
Visual — LED blinking
Slow blink = ready
✓
Pmod BT2 UART
Python serial + $$$ command
CMD response received
✓
UART Loopback
TXD0 → RXD0 jumper
b'hello' echoed back
✓
BT Pairing (Pi)
bluetoothctl pair
Paired and trusted
✓
BT Data Transfer
rfcomm + Python serial
Data received on UART
✓
Buzzer
pinctrl GPIO17 toggle
Audible buzz confirmed
✓
LED Red
pinctrl GPIO27 toggle
Red illuminated
✓
LED Green
pinctrl GPIO26 toggle
Green illuminated
✓
Emergency Mode
Simulated spike (step % 8)
LED flash + buzzer + OLED
✓
ThingsBoard MQTT
paho-mqtt publish
Data visible on dashboard
✓
Android BT
Serial Bluetooth Terminal app
Live data stream received
✓
Live Graph
smartband_plot.py
All 3 charts updating live
Smartband V001 · Hardware Integration & System Demonstration · Task 3 · HSHL 2026

## Slide 8
ISSUES ENCOUNTERED & RESOLUTIONS
Issue
Root Cause
Resolution
OLED not on i2cdetect
I2C not enabled on Pi
raspi-config → Interface Options → I2C
OLED blank screen
Wires in column j (not on extender)
Moved all wires to column e
Pmod no response to $$$
Pi 5 UART not on GPIO14/15 by default
Added enable_uart=1 to /boot/firmware/config.txt
BT CMD mode no response
Wrong serial device path
Used /dev/serial0 after enable_uart=1 reboot
BT pairing failed (passkey)
RN-42 uses fixed PIN, not passkey
Set SA,0 (no auth) + SP,1234 (PIN) via UART
Phone could not connect
Pi rfcomm occupied the module
Cleared SR,Z, switched to direct UART in v3
LED Green not lighting
Signal wire in GND row (a41)
Moved wire to LED Green row (a42)
font5x8.bin missing
File not in working directory
Downloaded from Adafruit GitHub to ~/smartband/
Smartband V001 · Hardware Integration & System Demonstration · Task 3 · HSHL 2026

## Slide 9
CONCLUSION & NEXT STEPS
Capabilities Delivered:
✓
Bluetooth SPP via Pmod BT2 — Android verified
✓
SSD1306 OLED — 5 display screens
✓
RGB LED + Buzzer emergency alerts
✓
ThingsBoard MQTT cloud telemetry
✓
Real-time matplotlib dashboard (3 charts)
✓
14 tests — all passed ✓
Next Steps:
→ Assemble Band01_Rev1 Smartband PCB hardware
→ Activate sensor calls in simple_peripheral.c and i2c_sensors.c
→ Replace simulated data with real BLE data from Smartband
→ Implement BLE scanning on Pi (bluepy/bleak) for CHAR1 0xFFF1
→ Integrate OledThread & AppThread (currently disabled in main.c)
→ Replace 0x7788 placeholder with real sensor readings
Smartband V001 · Masrur · Hochschule Hamm-Lippstadt (HSHL) · June 2026