## Slide 1
Citation & Literature Analysis
Smartband V001 Rev2 — HSHL Engineering Internship
Masrur Jamil Prochchhod
Matriculation No-22010028
Date-16/06/2026
Supervisor: Prof. Giovanni (giovannix)
Notes: Title slide. 20 papers analysed to support the Smartband V001 Rev2 internship at HSHL.

## Slide 2
The Paper Being Analysed — Pinheiro et al. (2022)
Multi-Sensor Wearable Health Device Framework
for Real-Time Monitoring of Elderly Patients
Frontiers in Human Neuroscience · Vol. 15 · Article 750591 · January 2022
Pinheiro GPM, Miranda RK, Praciano BJG, Santos GA, Mendonça FLL, Javidi E, da Costa JPJ & de Sousa RT Jr.
Proposes a complete healthcare framework combining a low-cost multi-sensor wristband, a high-resolution ESPRIT-based heart rate algorithm, and a 5-layer cloud monitoring application. Target cost: $25. Target population: elderly patients requiring contactless remote monitoring.
🔧 PILLAR 1 — HARDWARE
CC2640R2F MCU · MAX30102 PPG · MAX30205 Temp · LIS331DLTR IMU · 4-layer PCB · $25
🧮 PILLAR 2 — ALGORITHM
ESPRIT-based HR estimation via Hilbert Transform · outperforms FFT, autocorrelation, zero-crossing, peak detection
☁️ PILLAR 3 — SOFTWARE
5-layer monitoring app · REST API <213ms · Multi-patient · Multi-worker cloud dashboard
Notes: The Pinheiro 2022 paper is the core reference — all 20 analysed papers either support, compare, or extend this work.

## Slide 3
SECTION 1
Overview & Paper Categories
20 papers grouped by role and relevance

## Slide 4
How the 20 Papers Are Grouped by Category
☁️
Cloud / IoT
Healthcare
Papers: 1
Rev2 Firebase +
dashboards
Edge AI &
On-Device
Papers: 2, 8
nRF5340 edge
processing
🔩
Sensor Hardware
& Platforms
Papers: 3, 14
Rev2 multi-
sensor bus
👴
Clinical /
Elderly Studies
Papers: 4, 9, 11
Rev2 elderly
usability
👟
Gait &
Biomechanics
Papers: 5
IMU gait
analysis
🔬
Multi-Modal
Sensing Reviews
Papers: 6, 7, 13
Future Rev3
sensors
ML / AI
for Health
Papers: 15
Predictive
analytics
💊
PPG Theory
& HR Algorithms
Papers: 17–20
ESPRIT algorithm
baselines

## Slide 5
SECTION 2
Individual Paper Analyses
Papers 1–20: what each contributes, its limitations, and Rev2 relevance

## Slide 6
Papers 1 & 2 — Individual Analysis
1
CLOUD IOT
Syed et al. (2026) — AWS Cloud Patient Monitoring
CONTRIBUTES
End-to-end AWS IoT pipeline (IoT Core → Lambda → DynamoDB). Real-time vital sign monitoring for homecare patients with threshold-based alert escalation.
LIMITATION
No ML on sensor data — purely threshold-based alerts. AWS vendor lock-in. No clinical RMSE validation.
REV2
Rev2 Firebase Firestore mirrors the AWS pipeline. The three-tier architecture (device → Pi gateway → cloud) directly implements this paper's design pattern.
2
EDGE AI
Lhakshanaa et al. (2025) — Baseline-Adaptive Edge AI
CONTRIBUTES
92% anomaly detection accuracy, <1 second end-to-end alert latency. Adaptive per-patient baselines instead of fixed clinical thresholds.
LIMITATION
ESP32 processor too weak for ESPRIT-class algorithms. Lab-only validation, no real-world elderly testing.
REV2
nRF5340 in Rev2 far exceeds ESP32 — enables on-device adaptive alerting. The baseline-adaptive concept directly motivates Rev2's dashboard personalisation.

## Slide 7
Papers 3 & 4 — Individual Analysis
3
HARDWARE
Xiao et al. (2024) — Universal Multi-Sensor Readout
CONTRIBUTES
Universal wireless system reading ANY flexible sensor type (resistive, capacitive, piezoelectric). Modular architecture for heterogeneous sensor arrays.
LIMITATION
Research-grade only. No clinical outcomes. Form factor not optimised for daily elderly wear.
REV2
Rev2's sensor bus (MAX30102 on I2C, MAX30001 on SPI, ICM-42688-P on SPI, ICS-43434 on I2S) is exactly the heterogeneous multi-sensor problem this paper addresses.
4
CLINICAL
Donahue (2024) — Wearable Accelerometry & Cognition
CONTRIBUTES
Activity variability (diversity of movement patterns) predicts cognitive decline with OR=2.23 per SD decrease — outperforms raw step count. Rapid lung function decline → 84% higher dementia risk.
LIMITATION
Research accelerometers only. Activity variability not yet standardised clinically. No wearable deployment with elderly.
REV2
ICM-42688-P IMU in Rev2 captures the high-quality triaxial data needed. Activity variability metric can be added to Rev2 firmware as a zero-hardware-cost cognitive screening feature.

## Slide 8
Papers 5 & 6 — Individual Analysis
5
GAIT
Huang (2024) — BLE Smart Insoles & Gait Analysis
CONTRIBUTES
16-FSR pressure sensor insoles on nRF52840 (predecessor to nRF5340). GAN-based personalised plantar pressure models. BLE coexistence techniques for multi-device arrays.
LIMITATION
Separate insole device from wristband. GAN personalisation requires data collection sessions. No elderly fall-risk clinical validation.
REV2
nRF52840 → nRF5340 migration directly applicable. BLE coexistence management techniques are immediately relevant to Rev2 BLE 5.3 implementation.
6
REVIEW
Guarnaccia et al. (2026) — Convergent Sensing
CONTRIBUTES
Biometric + environmental multi-modal sensing produces composite health indices (stress, fitness, comfort). Context is essential to disambiguate physiological signals — same elevated HR can mean exercise, anxiety, or arrhythmia.
LIMITATION
Composite indices not yet clinically validated. Environmental MEMS sensors have stability issues for daily wear.
REV2
Rev2 BMP390L barometric pressure sensor begins convergent sensing. Future: adding gas/air-quality MEMS for full environmental context.

## Slide 9
Papers 7 & 8 — Individual Analysis
7
REVIEW
Kazanskiy et al. (2025) — Lab-on-Chip Biosensors
CONTRIBUTES
Miniaturised analytical processes for continuous biochemical sensing: glucose, lactate, hormones from sweat. Flexible rigid-flex PCB fabrication techniques. Future: wearable blood analysis without blood draws.
LIMITATION
Research-grade only. Long-term sensor stability <7 days. Manufacturing costs prohibitive for <$30 devices.
REV2
Maps Rev3 future trajectory. Current Rev2 FHIR R4 + Firebase infrastructure accommodates additional biochemical data streams without architectural change.
8
EMBEDDED SW
Toptsis et al. (2026) — Embedded SW Architecture
CONTRIBUTES
RTOS-based modular architectures outperform bare-metal for multi-sensor integration. Duty cycling, adaptive sampling, and load switching are the key battery management strategies.
LIMITATION
Architecture-focused only. No clinical performance benchmarks. Security architectures not deeply implemented.
REV2
Rev2 Zephyr RTOS on nRF5340 is exactly this architecture. TPS22918 load switches implement duty-cycling. This review validates every major Rev2 embedded software decision.

## Slide 10
Papers 9 & 10 — Individual Analysis
9
CLINICAL
Huang S. (2024) — Wearables for Elderly Safety
CONTRIBUTES
93.6% of elderly 60+ have at least one chronic condition (98.5% at 80+). Elderly-specific usability is the #1 deployment barrier — more important than technical accuracy.
LIMITATION
Qualitative review only. No controlled trial. Long-term compliance data (>3 months) limited.
REV2
Rev2's high-contrast OLED, DRV2605L haptic alerts, and SB- Band ID system-integrated registration directly address the usability barriers this paper identifies.
10
IOT/AI ARCHITECTURE
Shumba et al. (2022) — Three-Tier Edge Architecture
CONTRIBUTES
Three-tier hierarchy: device (<1ms alerts) → edge gateway (<100ms patterns) → cloud (analytics + ML). Pure cloud-to-device latency is too slow for life-critical alerts.
LIMITATION
Conceptual architecture only — no clinical prototype. Flexible piezoelectric sensors remain research-grade.
REV2
Rev2 already implements this exactly: nRF5340 (device) → Raspberry Pi 5 (edge) → Firebase (cloud). This paper validates Rev2's entire distributed architecture.

## Slide 11
Papers 11 & 12 — Individual Analysis
11
SYSTEMATIC REVIEW
Li et al. (2025) — IoT for Diabetic Elderly
CONTRIBUTES
29-paper systematic review. FHIR R4 explicitly recommended for IoT device interoperability. CGMs + smart dispensers significantly improve glycaemic control. Only 6/29 systems designed for elderly.
LIMITATION
Median study size ~40 participants. Follow-up typically <6 months. Device interoperability remains unsolved.
REV2
Directly validates Rev2's FHIR R4 implementation. Future: CGM API integration (Dexcom, FreeStyle Libre) for diabetes monitoring in the hospital dashboard.
12
ROBOTICS (METHOD)
de Koning & Jamshidnejad (2023) — Fuzzy Logic + MPC
CONTRIBUTES
Hierarchical combination of Model Predictive Control (formal optimisation) + Fuzzy Logic (human heuristics) for decision-making under sensor uncertainty. Better than either approach alone.
LIMITATION
Robotics context — requires significant adaptation for physiological signal processing.
REV2
Applicable to Rev2 alert logic: fuzzy logic on top of ESPRIT-estimated HR produces interpretable, patient-adaptive clinical alerts instead of rigid thresholds.

## Slide 12
Papers 13 & 14 — Individual Analysis
13
NOVEL SENSOR
Es Sebar et al. (2025) — Wearable Hydration Monitoring
CONTRIBUTES
Inkjet-printed interdigitated electrode sensors on polyimide substrate. EIS impedance at 199.5 Hz correlates linearly with skin hydration. Validates bioelectrical impedance for dehydration screening.
LIMITATION
In vitro validation only — no human data. Sweat interference not characterised. Readout circuit not yet miniaturised.
REV2
MAX30001 in Rev2 has BioZ mode for bioelectrical impedance analysis. Hydration monitoring is achievable with zero new hardware — a pure firmware enhancement.
14
OPEN HARDWARE
Alkhoury et al. (2026) — TinZr Open-Source Platform
CONTRIBUTES
25×25mm open-source ESP32-C3 wearable platform. Wi-Fi + BLE + IMU + microSD. All design files on GitHub. TinZrConnect Arduino library for rapid sensor integration.
LIMITATION
ESP32-C3 too weak for real-time ESPRIT. No regulatory compliance addressed. Wi-Fi consumes too much power for continuous monitoring.
REV2
TinZr's open-source philosophy aligns with Prof. Giovanni's GitHub approach. Rev2 firmware should publish similarly. TinZrConnect API architecture is a model for Rev2 nRF5340 firmware API.

## Slide 13
Papers 15 & 16 — Individual Analysis
15
AI / PREVENTION
Sharma et al. (2026) — AI Obesity Risk Prediction
CONTRIBUTES
ML classifiers (RF, SVM, decision trees) predict obesity risk from lifestyle data. AI-driven personalised nutrition intervention. Continuous wearable data identified as the critical missing input.
LIMITATION
Episodic clinical data only — not continuous wearable monitoring. Models not validated across diverse global populations.
REV2
Rev2 continuous physiological data (HR trends, HRV, activity patterns) is exactly what this review identifies as missing from current AI obesity models. FHIR R4 structures data for AI research pipelines.
16
PROCEEDINGS
ICTIS 2025 Proceedings — Springer
CONTRIBUTES
Conference proceedings containing Papers 2 & 3. Dedicated chapter on FHIR device authentication for IoT healthcare systems — identifies authentication as the critical missing security layer.
LIMITATION
Proceedings papers are short (8–12 pages), preliminary results only.
REV2
FHIR device authentication chapter directly addresses a Rev2 security gap. Must be implemented before any real patient data deployment.

## Slide 14
Papers 17 & 18 — Individual Analysis
17
PPG THEORY
Allen (2007) — PPG Signal Model
CONTRIBUTES
Mathematical PPG waveform model: x[n] = A·cos[2πfn + θ] + r[n]. AC component = cardiac pulses. DC component = breathing + autonomic nervous system. Frames HR detection as a frequency estimation problem.
LIMITATION
Pre-dates modern BLE wearables, integrated PPG sensors, and motion artefact methods. Does not address wrist movement noise.
REV2
This is Equation 1 of the Pinheiro paper — the foundation of ESPRIT-based HR. Rev2 MAX30102 signal processing pipeline is built directly on Allen's model.
18
ML HR ESTIMATION
Puranik & Morales (2020) — Adaptive NN Filter
CONTRIBUTES
Neural network learns the coupling between accelerometer motion and PPG motion artefact. Dynamically subtracts noise to recover clean cardiac signal. ~3% HR variation from medical reference.
LIMITATION
Per-user, per-activity training required. Not generalisable without retraining. Too computationally heavy for CC2640R2F.
REV2
ICM-42688-P IMU in Rev2 provides far higher-quality motion data than LIS331DLTR in Rev1 — directly improves artefact rejection quality. nRF5340 can run real-time adaptive filtering.

## Slide 15
Papers 19 & 20 — Individual Analysis
19
ML HR ESTIMATION
Xiong et al. (2017) — PCA + SVM Multi-Channel PPG
CONTRIBUTES
PCA → adaptive filter → SVM on multi-channel wrist PPG. 1.01 BPM RMSE during intense exercise. Spatial diversity from multiple channels improves noise separation.
LIMITATION
Requires multiple PPG channels → higher cost, complexity. SVM needs labelled training data. Multi-channel arrangement increases power consumption.
REV2
Rev2 uses single-channel PPG (MAX30102). Pinheiro shows ESPRIT single-channel ≈ Xiong multi-channel+SVM in most configs. Validates Rev2's simpler hardware choice.
20
DEEP LEARNING
Chung et al. (2020) — CNN + LSTM HR Estimation
CONTRIBUTES
CNN layers (local pattern detection) + LSTM layers (temporal tracking) on fused PPG + accelerometer spectra. ~1.5 BPM mean absolute error during exercise. Best-in-class for exercise scenarios.
LIMITATION
Requires labelled training data. Cannot run on CC2640R2F (128KB RAM). No power/latency benchmark on embedded hardware.
REV2
Primary TinyML target for Rev2. nRF5340 has 512KB RAM + hardware DSP → can run a quantised version. ICM-42688-P provides higher-quality accelerometer inputs than training datasets used.

## Slide 16
SECTION 3
Synthesis & Key Themes
What all 20 papers tell us together — and what it means for Rev2

## Slide 17
Five Major Themes Across All 20 Papers
🌐
Edge Intelligence
Is the Next Step
Papers 2, 8, 10
Three-tier: device (<1ms) → gateway (<100ms) → cloud. Pure cloud is too slow for life-critical alerts. Rev2 Pi gateway is the edge node.
🎯
Personalisation Over
Fixed Thresholds
Papers 2, 9, 15
Same HR value means different things for different patients. Systems must learn per-patient baselines. Fixed population averages cause false alarms.
📋
FHIR R4 Is the
Clinical Standard
Papers 10, 11, 16
Three independent research groups all call for FHIR R4 as the IoT interoperability standard. Rev2 has already implemented it — validated as the correct choice.
👴
Elderly Usability
Is the Key Barrier
Papers 9, 11
Usability matters more than accuracy for real-world adoption. Large fonts, haptic alerts, system-integrated registration — all in Rev2 already.
🔬
Multi-Modal Sensing
Beyond Vital Signs
Papers 6, 7, 13
Next generation: biometric + environmental + biochemical sensing. Rev2 BMP390L starts this journey. MAX30001 BioZ can add hydration — zero new hardware.

## Slide 18
Top 5 Immediate Rev2 Action Items (From Literature)
1
Cuffless Blood Pressure via PP-Net
Papers 13, 20
MAX30102 PPG already in Rev2 → add quantised PP-Net neural network on nRF5340. Estimates systolic + diastolic BP. Zero new hardware cost.
2
Hydration Monitoring via MAX30001 BioZ
Paper 13
MAX30001 BioZ mode → bioelectrical impedance analysis. Dehydration is a major elderly health risk. Zero new hardware.
3
Baseline-Adaptive Alert Logic
Papers 2, 9
Replace fixed vital sign thresholds in dashboards with per-patient learned baselines from Firestore history. Eliminates false alarm fatigue.
4
Activity Variability Metric
Paper 4
ICM-42688-P IMU captures 24h movement diversity. OR=2.23 for cognitive decline prediction. Zero hardware cost — pure firmware + dashboard.
5
FHIR Device Authentication
Paper 16
IoT device authentication is the critical missing security layer before real patient data can be used. Must implement before clinical deployment.

## Slide 19
Quick Reference — All 20 Papers at a Glance
# | Authors (Year) | Type | Core Finding | Rev2 Action
1 | Syed et al. (2026) | Cloud IoT | AWS end-to-end monitoring pipeline, threshold alerts | Firebase mirrors AWS architecture
2 | Lhakshanaa (2025) | Edge AI | 92% accuracy, <1s latency, adaptive baselines | Adaptive alerts on nRF5340
3 | Xiao et al. (2024) | Hardware | Universal multi-sensor wireless readout | Validates Rev2 sensor bus design
4 | Donahue (2024) | Clinical | Activity variability predicts dementia (OR=2.23) | IMU variability metric in firmware
5 | Huang (2024) | Gait | nRF52840 BLE smart insoles, GAN personalisation | BLE coexistence for nRF5340
6 | Guarnaccia (2026) | Review | Convergent biometric + environmental sensing | BMP390L environmental context
7 | Kazanskiy (2025) | Review | Lab-on-chip for glucose, ECG, neurophysiology | Future Rev3 biochemical sensors
8 | Toptsis (2026) | Embedded SW | RTOS modular architecture best practices | Validates Zephyr RTOS on nRF5340
9 | Huang S. (2024) | Clinical | 93.6% elderly 60+ have comorbidities; usability #1 barrier | OLED + haptic elderly design
10 | Shumba (2022) | Architecture | Three-tier edge/cloud validated | Confirms Rev2 distributed design
11 | Li et al. (2025) | Sys. Review | FHIR R4 needed for IoT interoperability | Validates Rev2 FHIR implementation
12 | de Koning (2023) | Robotics | Fuzzy logic + MPC for uncertain sensors | Adaptive alert decision engine
13 | Es Sebar (2025) | Sensor | EIS hydration monitoring, linear correlation | MAX30001 BioZ hydration mode
14 | Alkhoury (2026) | Open HW | TinZr: 25mm open-source wearable platform | Open-source Rev2 firmware model
15 | Sharma (2026) | AI | AI obesity prediction needs wearable data | Firestore data for AI pipelines
16 | ICTIS 2025 | Proceedings | FHIR device authentication chapter | Implement IoT authentication
17 | Allen (2007) | PPG Theory | x[n]=A·cos[2πfn+θ]+r[n] — PPG waveform model | MAX30102 signal processing base
18 | Puranik (2020) | ML HR | Adaptive NN + accel: 3% HR error | ICM-42688-P artefact rejection
19 | Xiong (2017) | ML HR | PCA+SVM multi-channel: 1.01 BPM | Validates single-channel PPG in Rev2
20 | Chung (2020) | Deep Learning | CNN+LSTM: 1.5 BPM, best for exercise | TinyML target for nRF5340

## Slide 20
Key Finding & Conclusion
Most Important Finding:
Cuffless blood pressure estimation is achievable in Rev2 using only the existing MAX30102 PPG sensor — via a quantised PP-Net neural network running on the nRF5340. No new hardware required. BP monitoring is the single highest-impact clinical enhancement across all 20 papers reviewed.
✅ BLE + FHIR R4 + Cloud
All 20 papers agree: this is the correct interoperability and connectivity architecture for clinical wearables.
✅ nRF5340-class Processor
Dual-core RTOS + DSP + 512KB RAM is the right embedded platform for multi-sensor health wearables in 2025–2026.
✅ Elderly Usability First
Large OLED display, haptic alerts, and system-integrated patient registration matter more than marginal sensor accuracy improvements.
Masrur Jamil Prochchhod · 2210028 · HSHL · Prof. Giovanni (giovannix) · June 2026
Notes: Conclude: Rev2 already addresses most gaps identified in the literature. The three remaining priorities are cuffless BP, hydration monitoring via BioZ, and FHIR device authentication.